## Slide 1: Learning Cycle
Discharge to empty
Relax >5hrs
Charge to full
Relax >2hrs
Discharge to empty
@ >C/10
Relax >5hrs

## Slide 2: Gauge Configuration – Learning Cycle (Step 1)
Discharge to empty
Option A
  Send IT_ENABLE command (0x0021)
    DataRAM:ControlStatus:RUP_DIS = 0
    DataFlash:IT_Enable = 1
  Send RESET command (0x0041)
    DataRAM:ControlStatus:RUP_DIS = 1
Relax >5hrs
Option B
  Send IT_ENABLE command (0x0021)
    DataRAM:ControlStatus:RUP_DIS = 0
    DataRAM:ControlStatus:VOK = QEN = 1
    DataFlash:IT_Enable = 1
    DataFlash:UpdateStatus = 00 (04 for pack-side gauge)
Learning cycle actually starts here!

## Slide 3: Gauge Configuration – Learning Cycle (Step 2)
Charge to full
Relax >2hrs
DataRAM:Flags:FC bit should -> 1 before charger shuts off!
charger shuts off
DataRAM:ControlStatus:VOK -> 0
DataFlash:Qmax0 -> updated
DataFlash:UpdateStatus -> 01
(05 for pack-side gauge)

## Slide 4: Gauge Configuration – Learning Cycle (Step 3)
Discharge to empty
@ >C/10
Relax >5hrs
Ra tables are updated during discharge
DataRAM:ControlStatus:VOK -> 0
DataFlash:Qmax0 -> updated
DataFlash:UpdateStatus -> 02
(06 for pack-side gauge)
Start discharge
(VOK will set again)