## Slide 1: AFE7950EVM & TSW14J56
3/21/2022

## Slide 2: Step 1: Open the AFE7900 Script Folder
Open Latte and navigate to the AFE7900 > bringup folder in the files dialog box on the left.
Scripts that are supported by the AFE7900 can be found in this location.

## Slide 3: Step 2: Establish Connection to AFE79xxEVM
Run the Setup & devInit scripts
After running both scripts you should get 1 error and 0 warnings.
The “Reset the FPGA and try again” error is expected and can be ignored because we are programming the TSW14J56 through HSDC Pro.

## Slide 4: Step 3: Configure FGPA to send data to DAC
Open HSDC Pro, connect to the board, and select AFE.
Go to the AFE TX tab.
Select AFE79xx_2x2TX_44210
Set the data rate to 491.52M
Create the tone
Press send
After pressing send, LED D3 on the AFE7950EVM will turn on

## Slide 5: Step 4: Configure AFE and LMK
Run the script titled S1_OnboardClk_RX250M_TX_FB_500M.
After running the script you should get 0 errors and 1 warning.
If you receive more errors and the JESD Links are not established press send in HSDC Pro again and type AFE.adcDacSync() in the Latte command line
After running the script D3 should be on and D2 should be blinking on the TSW14J56EVM
Notes: If you receive more errors and the JESD Links are not established press send in HSDC Pro again and type in the command AFE.adcDacSync()
  After

## Slide 6: Step 5a: Confirm the presence of Tx output
TxA NCO set to 9.5GHz
TxB NCO set to 9.5GHz

## Slide 7: Step 5b: Confirm the presence of Tx output
TxC NCO set to 9.5GHz
TxD NCO set to 9.5GHz

## Slide 8: Step 6: Configure HSDC Pro to Receive Rx Data
In HSDC Pro open the ADC tab and select the ‘AFE79xx_2x2RX_24410’ ini file
Change the ADC output data rate to 245.76MHz and Measurement Type to Complex FFT
Select the Data Capture Options Tab and select Capture Option
You can then change the # samples to 8192

## Slide 9: Step 7: Establishing ADC Link
You can now establish the ADC link by clicking capture.
D2 and D4 should now be flashing
  D1 and D3 should be off

## Slide 10: Step 8a: Confirm RxA and RxB captures
RxB:
NCO: 9.5 GHz
Input Freq: 9.52GHz
Input Level: 4.4 dBm
RxA:
NCO: 9.5 GHz
Input Freq: 9.52GHz
Input Level: 4.4 dBm

## Slide 11: Step 8b: Confirm RxC and RxD captures
RxD:
NCO: 9.5 GHz
Input Freq: 9.52GHz
Input Level: 4.9 dBm
RxC:
NCO: 9.5 GHz
Input Freq: 9.52GHz
Input Level: 4.4 dBm

## Slide 12: Step 9: Configure HSDC Pro to Receive Fb Data
In HSDC Pro select the ‘AFE79xx_1x2FB_44210’ ini file

## Slide 13: Step 10: Confirm FB1 and FB2 captures
FB2:
NCO: 9.5 GHz
Input Freq: 9.52 GHz
Input Level: 5.1 dBm
FB1:
NCO: 9.5 GHz
Input Freq: 9.52 GHz
Input Level: 5 dBm

## Slide 14: Step 11: Capture and send Data
You can now capture and send data from HSDC Pro