## Slide 1: LMG2175 SIMPLIS MODEL
User Guide

## Slide 2: Importing the Model
Include LMG2105R044_SIMPLIS.sxcmp in the same folder as the schematic(.sxsch).
Goto: Place -> Hierarchy -> Component(Relative Path) and select the model .sxcmp file.
Place the model into your circuit. It will look like this.

## Slide 3: Using the Model
Make the circuit and use the required pins as recommended in the datasheet.
Keep DHL,DLH and RDXX pins floating – guide for programming these pins is on the next page
You can use ZVDL and ZVDH pins in IIM mode
Example circuit – Buck Converter
BuckModel_LMG2105R044.sxsch is included for you reference.

## Slide 4: Programming DLH/DHL and RDXX pins
For DLH, DHL and RDXX pins –
Enter the value by double clicking this textbox to write the resistor values.
Enter ‘INF’ for floating the pin and ‘VCC’ when you want to connect it to VCC.
Press CRTL + S to save the file.
Go back to your circuit and run the simulation.
These are the recommended values for the pins.
Open the model file -
Click on the model and press CTRL + E to open the model file or
Right click on the model and select descend hierarchy.
The model file will look like this.

## Slide 5: Questions
If you face any issue with the model, please contact – m-wagle@ti.com or gan_apps@ti.com