## Slide 2
Diode need to be removed for proper VDS over current protection.
(Pls refer page 7)

## Slide 3
Should remove 10K ohm and 100pF to GND
(please refer page 7)
Should be connected to upper side of sense Resister (please refer page 8)
TI:Suggest Inline current sense
~1uF(DNP)
Close to FET is better for
EMI workaround as optional
~1uF(DNP)
Close to FET is better for
EMI workaround as optional
Suggest to remove 10K and 100pF

## Slide 4
Should remove 10K ohm and 100pF to GND
(please refer page 7)
Should be connected to upper side of sense Resister (please refer page 8)
TI:Suggest Inline current sense
~1uF(DNP)
Close to FET is better for
EMI workaround as optional
~1uF(DNP)
Close to FET is better for
EMI workaround as optional
Suggest to remove 10K and 100pF

## Slide 5
Should remove 10K ohm and 100pF to GND
(please refer page 7)
Should be connected to upper side of sense Resister (please refer page 8)
TI:Suggest Inline current sense
~1uF(DNP)
Close to FET is better for
EMI workaround as optional
~1uF(DNP)
Close to FET is better for
EMI workaround as optional
Suggest to remove 10K and 100pF

## Slide 6
Should remove 10K ohm and 100pF to GND
(please refer page 7)
Should be connected to upper side of sense Resister (please refer page 8)
TI:Suggest Inline current sense
~1uF(DNP)
Close to FET is better for
EMI workaround as optional
~1uF(DNP)
Close to FET is better for
EMI workaround as optional
Suggest to remove 10K and 100pF

## Slide 7
DRAIN pin should be connected “Drain of external FET” directly. DRAIN is used for VDS comparator

## Slide 8
DRV8718-Q1 can support Inline current sense. Could be preferable solution to measure the motor current waveform directly
PGNDx
PGNDx
InLine
LowSide