## Slide 1
SO1/SO2
To MCU
DNP (100nF)
Holding cap for CSA_Blanking if customer use CSA Blanking function
4.7ohm
47nF
Connect to source of external LS FET.
Please refer page 5 for details.
0ohm
0ohm 0402(inch) resistor:
Optional: helpful debug for EMC or workaround.

## Slide 2
0ohm on GHx and GLx.Optional. Can put some resister value if further slow down of tr/tf is needed.
To PGND1 pin
Please refer page 5
100nF(DNP)
Close to motor terminal.
EMI workaround as optional
~1uF(DNP)
Close to FET is better for
EMI workaround as optional

## Slide 3
0ohm on GHx and GLx.Optional. Can put some resister value if further slow down of tr/tf is needed.

## Slide 4
PI Filter ? This may be required for EMC. This is not TI DRV8718-Q1 requirement. PWM driving could need PI filter as EMC solution.
Just for your information.

## Slide 5
DRV8718-Q1 can support Inline current sense. Could be preferable solution to measure the motor current waveform directly
PGNDx
PGNDx
InLine
LowSide

## Slide 6
PGND1/PGND2/GND and decoupling in cap connection
1uF
PGND1 is source of low side gate drive for HB1/2.
PGND2 is for HB3/4.