## Slide 1: DRV832x (60V, 3-Phase BLDC Smart Gate Driver)
Power Tool / Garden Tool
Drone ESC & Gimbal
Robotic Servos
Vacuum Robot
Major Home Appliance
Small Home Appliance
Integrated Motor Modules
Medical Equipment
Wide operating voltage range for battery-powered and regulated supply applications
Reduced board space and system cost: gate driver, gate drive supply, gate drive setting resistors, sense amplifiers, and buck regulator integrated into small QFN package
Advanced on-chip protection with optional diagnostic reporting through SPI ensures a robust system
  Triple ½-H bridge motor gate driver
    Supply voltage: 6 to 60 V (abs max 65 V)
    Gate Drive: 1.0A source / 2.0A sink
  Smart Gate Drive eliminates 12-24 passive components
  Device selection options:
    SPI and H/W interface device options
    0- and 3- current shunt amplifier device options
    Optional integrated 600 mA buck converter
  6x/3x/1x PWM modes (including direct Hall sensor input)
  Adjustable dead time, VDS monitor, and gate drive current
  Fully Protected: Supply and charge pump undervoltage, overcurrent VDS monitors, gate driver faults, thermal warning and shutdown, sense amplifier overcurrent
Features
Benefits
Applications
5x5mm,32-pin - 7x7mm,48-pin
QFN package
Released!

## Slide 2: DRV832x (60V, 3-Phase BLDC Smart Gate Driver)
Released!
Single Microcontroller 18-V/600-W With Bluetooth® 5.0
36-V, 1-kW, 99% Efficient, 18-cm2 Power Stage
DRV832x Family App Note
25.2-V, 30-A High-speed sensorless (> 100 krpm)

## Slide 3: DRV832x Family (65-V 3-Phase BLDC Smart Gate Driver)
Released!
DRV8320RH
6x6 mm QFN
Gate driver
600 mA buck
H/W Interface
DRV8323H
6x6 mm QFN
Gate driver
3x Shunt amps
H/W Interface
DRV8320H
5x5 mm QFN
Gate driver
H/W Interface
DRV8323RH
7x7 mm QFN
Gate driver
600 mA buck
3x Shunt amps
H/W Interface
DRV8320RS
6x6 mm QFN
Gate driver
600 mA buck
SPI Interface
DRV8323S
6x6 mm QFN
Gate driver
3x Shunt amps
SPI Interface
DRV8320S
5x5 mm QFN
Gate driver
SPI Interface
DRV8323RS
7x7 mm QFN
Gate driver
600 mA buck
3x Shunt amps
SPI Interface

## Slide 4: DRV832x Features and Benefits
12, 24, 36 V batteries or regulated supplies
H/W for simple operation, SPI for more configuration
Optional 600 mA buck regulator
Optional triple current shunt amplifiers
Up to 1A source, 2A sink
Smart Gate Drive, no gate drive resistors, gate current is adjustable

## Slide 5: Current controlled architecture reduces external BOM
Smart gate driver (SGD) decrease the system bill of materials (BOM) and required board area.
Integrates 12-24 passive components for gate current setting (such as resistors and diodes).
Ability to adjust the MOSFET slew rate to trade off switching loss & EMI.
The RSOURCE and RSINK resistors manually adjust the gate source and sink current.
The diode lets the rise and fall VDS slew rates to be individually adjusted.
RPULLDOWN resistor makes sure that the MOSFET stays disabled even when the gate driver is inactive.
The SGD integrates high level protection:
    Over current, short circuit protection (VDS monitors)
    MOSFET gate handshake
    Gate-fault detection
    dV/dt turn-on prevention
Typical voltage controlled gate driver
DRV832x/DRV835x smart gate driver
Notes: 5

## Slide 6: Optimize the EMI and switching performance with IDRIVE DRV832x: Gate drive controllable from 10 mA to 1A source & 20 mA to 2A sink
Chart: SPI device current settings
1000 mA
10 mA
v
Chart: H/W device current settings
1000 mA
10 mA
v
Notes: 6

## Slide 7: DRV8323 & DRV8323R - Integrated current sense amplifiers
Gain options = 5, 10, 20, 40 V/V.
Offset calibration possible.
Sense amplifier can operate in bidirectional or unidirectional mode.
Unidirectional mode available on SPI only.
Current sense amplifier (CSA)
Sense amplifier - MOSFET VDS sense mode (SPI Only)
Eliminates the need of external shunt resistor and hence reduces cost and power loss.
The CSA amplify the voltage across the external low-side MOSFET VDS.
Notes: 7

## Slide 8: DRV832x PWM Control Modes - Four different PWM control modes to support various commutation and control methods
INLX | INHX | GLX | GHX | SHx
0 | 0 | L | L | Hi-Z
0 | 1 | L | H | H
1 | 0 | H | L | L
1 | 1 | L | L | Hi-Z
INLX | INHX | GLX | GHX | SHx
0 | X | L | L | Hi-Z
1 | 0 | H | L | L
1 | 1 | L | H | H
INLX | INHX | GLX | GHX
0 | 0 | L | L
0 | 1 | L | H
1 | 0 | H | L
1 | 1 | H | H
State | Logic/Hall Inputs |  |  |  |  |  | Gate Drive Outputs |  |  |  |  |  | Description
 | INHC = 0 |  |  | INHC = 1 |  |  | Phase A |  | Phase B |  | Phase C |  | 
 | INLA | INHB | INLB | INLA | INHB | INLB | GHA | GLA | GHB | GLB | GHC | GLC | 
Stop | 0 | 0 | 0 | 0 | 0 | 0 | L | L | L | L | L | L | Stop
Align | 1 | 1 | 1 | 1 | 1 | 1 | PWM | !PWM | L | H | L | H | Align
1 | 1 | 1 | 0 | 0 | 0 | 1 | L | L | PWM | !PWM | L | H | BC
2 | 1 | 0 | 0 | 0 | 1 | 1 | PWM | !PWM | L | L | L | H | AC
3 | 1 | 0 | 1 | 0 | 1 | 0 | PWM | !PWM | L | H | L | L | AB
4 | 0 | 0 | 1 | 1 | 1 | 0 | L | L | L | H | PWM | !PWM | CB
5 | 0 | 1 | 1 | 1 | 0 | 0 | L | H | L | L | PWM | !PWM | CA
6 | 0 | 1 | 1 | 1 | 0 | 1 | L | H | PWM | !PWM | L | L | BA
1x PWM mode uses 6-step block commutation tables that are stored internal to the gate driver.
Allows for a 3-phase BLDC motor to be controlled using one PWM sourced from a simple MCU.
1x PWM
6x PWM
3x PWM
Independent PWM
Notes: 8