## Slide 1: CDCE6214 Programming

## Slide 2: Write to EEPROM from Registers

## Slide 3: Using TICSPro

## Slide 4: Connect to Device
Power on device and Scan I2C as shown to the right
The default I2C address is 0x67

## Slide 5: Verify Config
Create or Load the desired config using the TICSPro GUI
Write All Registers and verify part is outputting as expected
Read All Registers and confirm desired config is properly displayed

## Slide 6: Select EEPROM Page
Using the drop down menu under Register Content Transfer, select which EEPROM page you want the current config to be written to
Select update_crc in the bottom corner

## Slide 7: Program EEPROM
Click Register to EEPROM
After EEPROM write is complete, you will see the following in the Status Box:
CRC of FILE and DEVICE values may be different than above, but they should be equal each other.
CRCERR should be 0x0000
After EEPROM write is complete, power cycle the device.

## Slide 8: For More Info
More info can be found in the EVM User’s Guide
https://www.ti.com/lit/ug/snau244a/snau244a.pdf

## Slide 9: Without TICSPro

## Slide 10: EEPROM Access

## Slide 11: Writing EEPROM Data from Registers
Power cycle the device after the EEPROM has finished being written to.

## Slide 12: For More Info
More info can be found in the Programming section of the Datasheet
https://www.ti.com/lit/ds/symlink/cdce6214.pdf

## Slide 13: Write to EEPROM from File

## Slide 14: Using TICSPro

## Slide 15: Connect to Device
Power on device and Scan I2C as shown to the right
The default I2C address is 0x67

## Slide 16: Program EEPROM
After EEPROM write is complete, you will see the following in the Status Box:
CRC of FILE and DEVICE values may be different than above, but they should be equal each other.
CRCERR should be 0x0000
After EEPROM write is complete, power cycle the device.

## Slide 17: Verify Config
Power on device
Connect to Device by Scanning for I2C
Read All Registers and verify config displayed is correct

## Slide 18: For More Info
More info can be found in the EVM User’s Guide
https://www.ti.com/lit/ug/snau244a/snau244a.pdf

## Slide 19: Without TICSPro

## Slide 20: EEPROM Access

## Slide 21: Writing EEPROM Data from File
Power cycle the device after the EEPROM has finished being written to.

## Slide 22: For More Info
More info can be found in the Programming section of the Datasheet
https://www.ti.com/lit/ds/symlink/cdce6214.pdf

## Slide 23: Reading EEPROM to File

## Slide 24: Using TICSPro

## Slide 25: Connect to Device
Power on device and Scan I2C as shown to the right
The default I2C address is 0x67

## Slide 26: Read EEPROM Content

## Slide 27: Adjust EEPROM File if needed
After the .hxt file has been exported, it may need to be adjusted
nvmlcrc and nvmscrc MUST be the same value. If they are different, change nvmscrc to match nvmlcrc
Byte 63 must also match nvmlcrc in both hex and decimal form
nvmcrcerr must be 0x0000