## Slide 1: CDCM6208 Phase Noise
September 16, 2025
DCC-CTS

## Slide 2: Test Setup
CDCM6208V1 is configured with the customer provided register values
Only the external loop filter values are changed between captures
Captures are taken on Y2

## Slide 3: Base Internal Loop Filter Values

## Slide 4: Input Reference
Jitter: 1.4ps
10kHz offset: -142dBc/Hz

## Slide 5: Configuration 1
C1=100pF, R2=500, C2=22nF
Jitter: 615fs
10kHz offset: -144dBc/Hz

## Slide 6: Configuration 2
C1=220pF, R2=400, C2=22nF
Jitter: 582fs
10kHz offset: -136dBc/Hz

## Slide 7: Configuration 3
C1=4.7uF, R2=145, C2=47uF
Jitter: 826fs
10kHz offset: -113dBc/Hz

## Slide 8: Configuration 4
C1=1uF, R2=1.3k, C2=22uF
Jitter: 1.03ps
10kHz offset: -104dBc/Hz