## Slide 1: DPLL Comparison with Si5381A-E13960-GM
June 03 2025
Clocks and Timing Solutions

## Slide 2
Feature |  | Si5381A-E13960-GM | LMK05028
APLL | # APLL | 4 (4x LC VCO) | 2 (2x LC VCO)
 | Oscillator | 54 MHz | XO: 10 MHz to 100 MHz TCXO: 10 MHz to 54 MHz
 | DCO / PTP support | No | No
DPLL | # DPLL | 4 | 2
 | # Inputs | 4 differential or 4 single-ended | 4 differential or 4 single-ended
 | Programable BW | 1 Hz to 4 kHz | 1 mHz to 4 kHz
 | Input Frequency | 8 kHz to 750 MHz (250 MHz max for CMOS) | 2 MHz to 750 MHz (250 MHz max for CMOS)
 | Hitless Switching | Yes | Yes
 | Holdover | Yes | Yes
 | Zero-Delay Mode | Yes | Yes
 | 1PPS IN/OUT | No | No 1PPS input, yes 1PPS output.
 | DCO / PTP support | Yes | Yes (40 bit, <1 ppt)
Outputs | # Outputs | 12 differential outputs or 24 CMOS | 8 differential outputs or 16 CMOS
 | SYSREF | Yes | No
 | Output Frequency | 100 Hz to 2.94912 GHz | 1 Hz to 750 MHz (200 MHz max for CMOS)
 | Formats | LVDS, AC-LVPECL, AC-CML, AC-HCSL, LVCMOS (1.8, 2.5, or 3.3 V) | AC-LVDS, AC-LVPECL, AC-CML, HCSL, LVCMOS (1.8 or 2.65 V)
 | RMS Jitter (12 kHz to 20 MHz) | 88 fs typ at 156.25 MHz 72 fs typ at 122.88 MHz | 150 fs typ at 156.25 MHz 160 fs typ at 122.88 MHz
 | Core and Output Power Supply | Core: 1.8 V, 3.3 V and Output: 1.8, 2.5, or 3.3 V | Core: 3.3 V and Output: 1.8, 2.5, or 3.3 V
Package Size |  | 9x9 mm QFN-64 | 9x9 mm VQFN-64

## Slide 3
Feature |  | Si5381A-E13960-GM | LMK05318B or LMK05318B-Q1
APLL | # APLL | 4 (4x LC VCO) | 2 (1x LC VCO + 1x BAW VCO)
 | Oscillator | 54 MHz | 10 MHz to 100 MHz (XO, TCXO, or OCXO)
 | DCO / PTP support | No | No
DPLL | # DPLL | 4 | 1
 | # Inputs | 4 differential or 4 single-ended | 2 differential or 2 single-ended
 | Programable BW | 1 Hz to 4 kHz | 1 mHz to 4 kHz
 | Input Frequency | 8 kHz to 750 MHz (250 MHz max for CMOS) | 0.5 Hz to 800 MHz (200 MHz max for CMOS)
 | Hitless Switching | Yes | Yes
 | Holdover | Yes | Yes
 | Zero-Delay Mode | Yes | No
 | 1PPS IN/OUT | No | Yes (PRIREF and OUT7 only)
 | DCO / PTP support | Yes | Yes (40 bit, <1 ppt)
Outputs | # Outputs | 12 differential outputs or 24 CMOS | 8 differential outputs or 4 differential with 4 CMOS
 | SYSREF | Yes | No
 | Output Frequency | 100 Hz to 2.94912 GHz | 1 Hz to 1250 MHz (200 MHz max for CMOS)
 | Formats | LVDS, AC-LVPECL, AC-CML, AC-HCSL, LVCMOS (1.8, 2.5, or 3.3 V) | AC-LVDS, AC-LVPECL, AC-CML, HCSL, LVCMOS (1.8 or 2.65 V)
 | RMS Jitter (12 kHz to 20 MHz) | 88 fs typ at 156.25 MHz 72 fs typ at 122.88 MHz | 50 fs typ at 312.5 MHz 60 fs typ at 156.25 MHz 145 fs typ at 155.52 MHz
 | Core and Output Power Supply | Core: 1.8 V, 3.3 V and Output: 1.8, 2.5, or 3.3 V | Core: 3.3 V and Output: 1.8, 2.5, or 3.3 V
Package Size |  | 9x9 mm QFN-64 | 7x7 mm VQFN-48

## Slide 4
Feature |  | Si5381A-E13960-GM | LMK5B12204
APLL | # APLL | 4 (4x LC VCO) | 2 (1x LC VCO + 1x BAW VCO)
 | Oscillator | 54 MHz | 10 MHz to 100 MHz (XO, TCXO, or OCXO)
 | DCO / PTP support | No | No
DPLL | # DPLL | 4 | 1
 | # Inputs | 4 differential or 4 single-ended | 2 differential or 2 single-ended
 | Programable BW | 1 Hz to 4 kHz | 1 mHz to 4 kHz
 | Input Frequency | 8 kHz to 750 MHz (250 MHz max for CMOS) | 0.5 Hz to 800 MHz (200 MHz max for CMOS)
 | Hitless Switching | Yes | Yes
 | Holdover | Yes | Yes
 | Zero-Delay Mode | Yes | No
 | 1PPS IN/OUT | No | Yes (PRIREF and OUT7 only)
 | DCO / PTP support | Yes | Yes (40 bit, <1 ppt)
Outputs | # Outputs | 12 differential outputs or 24 CMOS | 4 differential outputs or 2 differential with 4 CMOS
 | SYSREF | Yes | No
 | Output Frequency | 100 Hz to 2.94912 GHz | 1 Hz to 1250 MHz (200 MHz max for CMOS)
 | Formats | LVDS, AC-LVPECL, AC-CML, AC-HCSL, LVCMOS (1.8, 2.5, or 3.3 V) | AC-LVDS, AC-LVPECL, AC-CML, HCSL, LVCMOS (1.8 or 2.65 V)
 | RMS Jitter (12 kHz to 20 MHz) | 88 fs typ at 156.25 MHz 72 fs typ at 122.88 MHz | 50 fs typ at 312.5 MHz 60 fs typ at 156.25 MHz 145 fs typ at 155.52 MHz
 | Core and Output Power Supply | Core: 1.8 V, 3.3 V and Output: 1.8, 2.5, or 3.3 V | Core: 3.3 V and Output: 1.8, 2.5, or 3.3 V
Package Size |  | 9x9 mm QFN-64 | 7x7 mm VQFN-48

## Slide 5
Feature |  | Si5381A-E13960-GM | LMK5C33216A
APLL | # APLL | 4 (4x LC VCO) | 3 (2x LC VCO + 1x BAW VCO)
 | Oscillator | 54 MHz | 10 MHz to 156.25 MHz (XO, TCXO, or OCXO)
 | DCO / PTP support | No | Yes
DPLL | # DPLL | 4 | 3
 | # Inputs | 4 differential or 4 single-ended | 2 differential or 2 single-ended
 | Programable BW | 1 Hz to 4 kHz | 1 mHz to 4 kHz
 | Input Frequency | 8 kHz to 750 MHz (250 MHz max for CMOS) | 0.5 Hz to 800 MHz (200 MHz max for CMOS)
 | Hitless Switching | Yes | Yes
 | Holdover | Yes | Yes
 | Zero-Delay Mode | Yes | Yes (all internal)
 | 1PPS IN/OUT | No | Yes
 | DCO / PTP support | Yes | Yes (40 bit)
Outputs | # Outputs | 12 differential outputs or 24 CMOS | 16 differential outputs or 14 differential with 6 CMOS
 | SYSREF | Yes | Yes
 | Output Frequency | 100 Hz to 2.94912 GHz | 1 Hz to 1250 MHz (200 MHz max for CMOS)
 | Formats | LVDS, AC-LVPECL, AC-CML, AC-HCSL, LVCMOS (1.8, 2.5, or 3.3 V) | LVDS, AC-LVPECL, AC-CML, HCSL, LVCMOS (1.8 or 2.65 V)
 | RMS Jitter (12 kHz to 20 MHz) | 88 fs typ at 156.25 MHz 72 fs typ at 122.88 MHz | 40 fs typ at 491.52 MHz 55 fs typ at 122.88 MHz 110 fs typ at 156.25 MHz
 | Core and Output Power Supply | Core: 1.8 V, 3.3 V and Output: 1.8, 2.5, or 3.3 V | Core: 3.3 V and Output: 3.3 V
Package Size |  | 9x9 mm QFN-64 | 9x9 mm VQFN-64

## Slide 6
Feature |  | Si5381A-E13960-GM | LMK5C33414A
APLL | # APLL | 4 (4x LC VCO) | 3 (2x LC VCO + 1x BAW VCO)
 | Oscillator | 54 MHz | 10 MHz to 156.25 MHz (XO, TCXO, or OCXO)
 | DCO / PTP support | No | Yes
DPLL | # DPLL | 4 | 3
 | # Inputs | 4 differential or 4 single-ended | 4 differential or 4 single-ended
 | Programable BW | 1 Hz to 4 kHz | 1 mHz to 4 kHz
 | Input Frequency | 8 kHz to 750 MHz (250 MHz max for CMOS) | 0.5 Hz to 800 MHz (200 MHz max for CMOS)
 | Hitless Switching | Yes | Yes
 | Holdover | Yes | Yes
 | Zero-Delay Mode | Yes | Yes (all internal)
 | 1PPS IN/OUT | No | Yes
 | DCO / PTP support | Yes | Yes (40 bit)
Outputs | # Outputs | 12 differential outputs or 24 CMOS | 14 differential outputs or 12 differential with 6 CMOS
 | SYSREF | Yes | Yes
 | Output Frequency | 100 Hz to 2.94912 GHz | 1 Hz to 1250 MHz (200 MHz max for CMOS)
 | Formats | LVDS, AC-LVPECL, AC-CML, AC-HCSL, LVCMOS (1.8, 2.5, or 3.3 V) | LVDS, AC-LVPECL, AC-CML, HCSL, LVCMOS (1.8 or 2.65 V)
 | RMS Jitter (12 kHz to 20 MHz) | 88 fs typ at 156.25 MHz 72 fs typ at 122.88 MHz | 40 fs typ at 491.52 MHz 55 fs typ at 122.88 MHz 110 fs typ at 156.25 MHz
 | Core and Output Power Supply | Core: 1.8 V, 3.3 V and Output: 1.8, 2.5, or 3.3 V | Core: 3.3 V and Output: 3.3 V
Package Size |  | 9x9 mm QFN-64 | 9x9 mm VQFN-64

## Slide 7
Feature |  | Si5381A-E13960-GM | LMK5C22212A
APLL | # APLL | 4 (4x LC VCO) | 2 (1x LC VCO + 1x BAW VCO)
 | Oscillator | 54 MHz | 10 MHz to 156.25 MHz (XO, TCXO, or OCXO)
 | DCO / PTP support | No | Yes
DPLL | # DPLL | 4 | 2
 | # Inputs | 4 differential or 4 single-ended | 2 differential or 2 single-ended
 | Programable BW | 1 Hz to 4 kHz | 1 mHz to 4 kHz
 | Input Frequency | 8 kHz to 750 MHz (250 MHz max for CMOS) | 0.5 Hz to 800 MHz (200 MHz max for CMOS)
 | Hitless Switching | Yes | Yes
 | Holdover | Yes | Yes
 | Zero-Delay Mode | Yes | Yes (all internal)
 | 1PPS IN/OUT | No | Yes
 | DCO / PTP support | Yes | Yes (40 bit)
Outputs | # Outputs | 12 differential outputs or 24 CMOS | 12 differential outputs or 10 differential with 6 CMOS
 | SYSREF | Yes | Yes
 | Output Frequency | 100 Hz to 2.94912 GHz | 1 Hz to 1250 MHz (200 MHz max for CMOS)
 | Formats | LVDS, AC-LVPECL, AC-CML, AC-HCSL, LVCMOS (1.8, 2.5, or 3.3 V) | LVDS, AC-LVPECL, AC-CML, HCSL, LVCMOS (1.8 or 2.65 V)
 | RMS Jitter (12 kHz to 20 MHz) | 88 fs typ at 156.25 MHz 72 fs typ at 122.88 MHz | 40 fs typ at 491.52 MHz 55 fs typ at 122.88 MHz 110 fs typ at 156.25 MHz
 | Core and Output Power Supply | Core: 1.8 V, 3.3 V and Output: 1.8, 2.5, or 3.3 V | Core: 3.3 V and Output: 3.3 V
Package Size |  | 9x9 mm QFN-64 | 9x9 mm VQFN-64

## Slide 8
Feature |  | Si5381A-E13960-GM | LMK5C23208A
 | # APLL | 4 (4x LC VCO) | 3 (2x LC VCO + 1x BAW VCO)
 | Oscillator | 54 MHz | 10 MHz to 156.25 MHz (XO, TCXO, or OCXO)
 | DCO / PTP support | No | Yes
 | # DPLL | 4 | 2
 | # Inputs | 4 differential or 4 single-ended | 2 differential or 2 single-ended
 | Programable BW | 1 Hz to 4 kHz | 1 mHz to 4 kHz
 | Input Frequency | 8 kHz to 750 MHz (250 MHz max for CMOS) | 0.5 Hz to 800 MHz (200 MHz max for CMOS)
 | Hitless Switching | Yes | Yes
 | Holdover | Yes | Yes
 | Zero-Delay Mode | Yes | Yes (all internal)
 | 1PPS IN/OUT | No | Yes
 | DCO / PTP support | Yes | Yes (40 bit, <1 ppt)
 | # Outputs | 12 differential outputs or 24 CMOS | 16 differential outputs or 14 differential with 6 CMOS
 | SYSREF | Yes | Yes
 | Output Frequency | 100 Hz to 2.94912 GHz | 1 Hz to 1250 MHz (200 MHz max for CMOS)
 | Formats | LVDS, AC-LVPECL, AC-CML, AC-HCSL, LVCMOS (1.8, 2.5, or 3.3 V) | LVDS, AC-LVPECL, AC-CML, HCSL, LVCMOS (1.8 or 2.65 V)
 | RMS Jitter (12 kHz to 20 MHz) | 88 fs typ at 156.25 MHz 72 fs typ at 122.88 MHz | 40 fs typ at 491.52 MHz 55 fs typ at 122.88 MHz 110 fs typ at 156.25 MHz
 | Core and Output Power Supply | Core: 1.8 V, 3.3 V and Output: 1.8, 2.5, or 3.3 V | Core: 3.3 V and Output: 3.3 V
Package Size |  | 9x9 mm QFN-64 | 9x9 mm VQFN-64

## Slide 9
Feature |  | Si5381A-E13960-GM | LMK5B33414
APLL | # APLL | 4 (4x LC VCO) | 3 (2x LC VCO + 1x BAW VCO)
 | Oscillator | 54 MHz | 10 MHz to 156.25 MHz (XO, TCXO, or OCXO)
 | DCO / PTP support | No | Yes
DPLL | # DPLL | 4 | 3
 | # Inputs | 4 differential or 4 single-ended | 4 differential or 4 single-ended
 | Programable BW | 1 Hz to 4 kHz | 1 mHz to 4 kHz
 | Input Frequency | 8 kHz to 750 MHz (250 MHz max for CMOS) | 0.5 Hz to 800 MHz (200 MHz max for CMOS)
 | Hitless Switching | Yes | Yes
 | Holdover | Yes | Yes
 | Zero-Delay Mode | Yes | Yes (all internal)
 | 1PPS IN/OUT | No | Yes
 | DCO / PTP support | Yes | Yes (40 bit)
Outputs | # Outputs | 12 differential outputs or 24 CMOS | 14 differential outputs or 12 differential with 6 CMOS
 | SYSREF | Yes | Yes
 | Output Frequency | 100 Hz to 2.94912 GHz | 1 Hz to 1250 MHz (200 MHz max for CMOS)
 | Formats | LVDS, AC-LVPECL, AC-CML, AC-HCSL, LVCMOS (1.8, 2.5, or 3.3 V) | LVDS, AC-LVPECL, AC-CML, HCSL, LVCMOS (1.8 or 2.65 V)
 | RMS Jitter (12 kHz to 20 MHz) | 88 fs typ at 156.25 MHz 72 fs typ at 122.88 MHz | 42 fs typ at 312.5 MHz 47 fs typ at 156.25 MHz 110 fs typ at 122.88 MHz
 | Core and Output Power Supply | Core: 1.8 V, 3.3 V and Output: 1.8, 2.5, or 3.3 V | Core: 3.3 V and Output: 3.3 V
Package Size |  | 9x9 mm QFN-64 | 9x9 mm VQFN-64

## Slide 10
Feature |  | Si5381A-E13960-GM | LMK5B33216
APLL | # APLL | 4 (4x LC VCO) | 3 (2x LC VCO + 1x BAW VCO)
 | Oscillator | 54 MHz | 10 MHz to 156.25 MHz (XO, TCXO, or OCXO)
 | DCO / PTP support | No | Yes
DPLL | # DPLL | 4 | 3
 | # Inputs | 4 differential or 4 single-ended | 2 differential or 2 single-ended
 | Programable BW | 1 Hz to 4 kHz | 1 mHz to 4 kHz
 | Input Frequency | 8 kHz to 750 MHz (250 MHz max for CMOS) | 0.5 Hz to 800 MHz (200 MHz max for CMOS)
 | Hitless Switching | Yes | Yes
 | Holdover | Yes | Yes
 | Zero-Delay Mode | Yes | Yes (all internal)
 | 1PPS IN/OUT | No | Yes
 | DCO / PTP support | Yes | Yes (40 bit)
Outputs | # Outputs | 12 differential outputs or 24 CMOS | 16 differential outputs or 14 differential with 6 CMOS
 | SYSREF | Yes | Yes
 | Output Frequency | 100 Hz to 2.94912 GHz | 1 Hz to 1250 MHz (200 MHz max for CMOS)
 | Formats | LVDS, AC-LVPECL, AC-CML, AC-HCSL, LVCMOS (1.8, 2.5, or 3.3 V) | LVDS, AC-LVPECL, AC-CML, HCSL, LVCMOS (1.8 or 2.65 V)
 | RMS Jitter (12 kHz to 20 MHz) | 88 fs typ at 156.25 MHz 72 fs typ at 122.88 MHz | 42 fs typ at 312.5 MHz 47 fs typ at 156.25 MHz 110 fs typ at 122.88 MHz
 | Core and Output Power Supply | Core: 1.8 V, 3.3 V and Output: 1.8, 2.5, or 3.3 V | Core: 3.3 V and Output: 3.3 V
Package Size |  | 9x9 mm QFN-64 | 9x9 mm VQFN-64

## Slide 11
Feature |  | Si5381A-E13960-GM | LMK5B12212
APLL | # APLL | 4 (4x LC VCO) | 2 (1x LC VCO + 1x BAW VCO)
 | Oscillator | 54 MHz | 10 MHz to 156.25 MHz (XO, TCXO, or OCXO)
 | DCO / PTP support | No | Yes
DPLL | # DPLL | 4 | 1
 | # Inputs | 4 differential or 4 single-ended | 2 differential or 2 single-ended
 | Programable BW | 1 Hz to 4 kHz | 1 mHz to 4 kHz
 | Input Frequency | 8 kHz to 750 MHz (250 MHz max for CMOS) | 0.5 Hz to 800 MHz (200 MHz max for CMOS)
 | Hitless Switching | Yes | Yes
 | Holdover | Yes | Yes
 | Zero-Delay Mode | Yes | Yes (all internal)
 | 1PPS IN/OUT | No | Yes
 | DCO / PTP support | Yes | Yes (40 bit)
Outputs | # Outputs | 12 differential outputs or 24 CMOS | 12 differential outputs or 10 differential with 6 CMOS
 | SYSREF | Yes | Yes
 | Output Frequency | 100 Hz to 2.94912 GHz | 1 Hz to 1250 MHz (200 MHz max for CMOS)
 | Formats | LVDS, AC-LVPECL, AC-CML, AC-HCSL, LVCMOS (1.8, 2.5, or 3.3 V) | LVDS, AC-LVPECL, AC-CML, HCSL, LVCMOS (1.8 or 2.65 V)
 | RMS Jitter (12 kHz to 20 MHz) | 88 fs typ at 156.25 MHz 72 fs typ at 122.88 MHz | 42 fs typ at 312.5 MHz 47 fs typ at 156.25 MHz 110 fs typ at 122.88 MHz
 | Core and Output Power Supply | Core: 1.8 V, 3.3 V and Output: 1.8, 2.5, or 3.3 V | Core: 3.3 V and Output: 3.3 V
Package Size |  | 9x9 mm QFN-64 | 9x9 mm VQFN-64