## Slide 1: LMK05318B Register Changes
CTS

## Slide 2: Rev ID (R3[7:0])
LMK05318:
  0b00010001
LMK05318B:
  Initial RTM: 0b00110010
  Post PCN: 0b01000010

## Slide 3: R40[3:0]
Default value:
  0b0000
Non-B version:
  Reserved (Spare NVM register).
B version:
  Bit 3: SECREF_DC_MODE
  Bit 2: PRIREF_DC_MODE
  Bit 1: Reserved
  Bit 0: APLL2_DEN_MODE

## Slide 4: R45[1:0]
Default value:
  0b11
Non-B version:
  Reserved.
B version:
  Bit 1: SECREF_BUF_MODE
  Bit 0: PRIREF_BUF_MODE

## Slide 5: Combined explanation of R40[3:2] and R45[1:0]
R40[3] | R45[1] | SECREF Input Buffer
0 | 0 | Set AC coupled buffer offset voltage to 50mV
0 | 1 | Set AC coupled buffer offset voltage to 200mV
1 | 0 | Enable DC hysteresis
1 | 1 | Disable DC hysteresis
R40[2] | R45[0] | PRIREF Input Buffer
0 | 0 | Set AC coupled buffer offset voltage to 50mV
0 | 1 | Set AC coupled buffer offset voltage to 200mV
1 | 0 | Enable DC hysteresis
1 | 1 | Disable DC hysteresis

## Slide 6: R39[0]
Default value:
  0b0
Non-B version:
  Reserved (spare NVM register)
B version:
  APLL1_DEN_MODE

## Slide 7: APLL1 fractional divider (R110-R114, R339)
Default values:
  0x0 for all 6 registers (R110-R114, R339)
Non-B version:
  R110: PLL1_NUM[39:32]
  R111: PLL1_NUM[31:24]
  R112: PLL1_NUM[23:16]
  R113: PLL1_NUM[15:8]
  R114: PLL1_NUM[7:0]
  R339: DPLL unlock detect register.
B version:
  If APLL1_DEN_MODE = 0, R110-R114 same as above; R339 is unused.
  If APLL1_DEN_MODE = 1:
    R339, R110, R111 = 24-bit APLL1 numerator [23:16], [15:8], [7:0]
    R112, R113, R114 = 24-bit APLL1 denominator [23:16], [15:8], [7:0]
    Find more details in the register manual.

## Slide 8: APLL2 fractional divider (R333-R335)
Default value:
  0x0 for all 3 registers (R333-R335)
Non-B version:
  DPLL unlock detect registers
B version:
  If APLL2_DEN_MODE = 0, R333-R335 are unused.
  If APLL2_DEN_MODE = 1:
    R333: PLL2_DEN[23:16]
    R334: PLL2_DEN[15:8]
    R335: PLL2_DEN[7:0]