## Slide 1: Enter PBTL mode for CH1/2, BTL mode for CH3 and CH4
2. Set buttons on EVM as below
up
up
up
down
3. Toggle PDN button, set buttons on EVM as below
down
up
up
down
4. Click “I2C” button on below, then a window pop up
5. Run below script, to set CH1/2 into PBTL mode
w c0 02 04
(Note: C0 is device address)
1. Make sure the blue block is at “IO”
2. Write “w c0 02 04”
3. Click “Execute” button
6. Toggle STBY button, set buttons as below
down
up
down
down
1. Power up and connect EVM (keep the PDN and STBY button down), goes into Device Monitor & Control First.