## Slide 1
Page | Register | Bit | R/W | Value | Comment
 | 0 | D7-0 | R/W | 0 | Page 0 selected
Step1 : Access to Page 0
Page | Register | Bit | R/W | Value | Comment
0 | 82 | D7 | R/W | 1 | ADC(CH1) muted
0 | 82 | D3 | R/W | 1 | ADC(CH2) muted
0 | 81 | D7 | R/W | 0 | ADC(CH1) Powered down
0 | 81 | D6 | R/W | 0 | ADC(CH2) Powered down
Step2 : ADC muted and powered down
Step3 :Wait >= 100ms
Page | Register | Bit | R/W | Value | Comment
 | 0 | D7-0 | R/W | 4 | Page 4 selected
Step4 : Access to Page 4
Step5 : Write value to registers
Page | Register | Bit | R/W | Value | Comment
4 | 12 | D7-0 | R/W | 0xFF | 
4 | 13 | D7-0 | R/W | 0xFF | 

## Slide 2
Step6 : Access to Register 0
Page | Register | Bit | R/W | Value | Comment
 | 0 | D7-0 | R/W | 0 | Page 0 selected
Step7 : ADC powered up , and ADC unmuted
Page | Register | Bit | R/W | Value | Comment
0 | 81 | D7 | R/W | 1 | ADC (CH1) powered up
0 | 81 | D6 | R/W | 1 | ADC (CH2) powered up
0 | 82 | D7 | R/W | 0 | ADC (CH1) unmuted
0 | 82 | D3 | R/W | 0 | ADC (CH2) unmuted
Step8 :Wait >= 100ms (for ADC stable)