## Slide 1: TAS6584 RTLDG SW Flow and Script
TI-Audio-MPA

## Slide 2: Realtime diagnostic flow
Initialization script is on page #3. The setting is basic configuration.
Before enable Real-time diag, DC diag detection should have no error. DC diagnostic script is on page #4.
Once RTLDG fault is triggered, 0x72, 0x73 channels registers will report fault. Read 0x8B, 0x8C RTLDG fault registers and 0x72, 0x73 channels registers to confirm RTLDG fault triggered.
Once RTLDG fault is triggered, Real-time should be disabled, then clear Real-time fault and DSP buffer. The script is on page #6 and #7.
The reference scripts are attached, please see below scripts.
Initialization(page #3)
Run DC load diagnostic(page #4)
(DC diag fail count++)
Check 0x072, 0x73
channels status.
Is in DC diag?
Y
N
Read DC diag result,
Is load status good?
N
DC diag fail count > N
N
Y
Notify end user
Y
Initiation of pilot tone and RTLDG(page #5)
End
Check 0x8B, 0x8C
RTLDG status and 0x72, 0x73 channel status.
Fault reported?
N
Y
RTLDG fail count ++
Disable RTLDG
RTLDG Clear fault(page #6 and #7)
RTLDG diag fail count > N
Notify end user
N
Y

## Slide 3: Initialization
w C0 00 00 # Page switching (1st 00) to page 0 (2nd 00)
w C0 7F 00 # Change to book 00. It's required to be in page 0 before changing a book
w C0 00 00 # Go to the page 0 in book 00
w c0 01 01 #Clear reg
d 100
## Set Channels to SLEEP state ##
w C0 03 22 # Set Channel 1#2 to SLEEP state
w C0 04 22 # Set Channel 3#4 to SLEEP state
w C0 9F 10 # Configure GPIO_1 to become SDIN2
w C0 05 00 # Current Sense disabled on all channels
w C0 61 02 # Enable Random Spread Spectrum
w C0 1D 00 # Sample rate: Auto detect
w C0 AA 04 # Disable Dynamic Range Boost (DRBoost)
w C0 4E 80 # Enable Analog gain ramp up#down, set 60us#step
w C0 93 4F # Enable Clip detect
w C0 54 00 # Disable CBC Warn and CBC Fault
w C0 52 01 # Set Fsw to 480 KHz
w C0 02 01 # Set 1SPW Modulation
################## Set bandwidth depending on Fsw
w C0 6D 19 # Use for 480 kHz Fsw, Bandwidth setting to 150K.
##################
## Set Channels to Hi-Z state ##
w C0 03 33 # Set Channel 1#2 to Hi-Z state
w C0 04 33 # Set Channel 3#4 to Hi-Z state

## Slide 4: DC diagnostic
## Run channels DC diag ##
w C0 03 11 # Channel 1#2 run DC diag
w C0 04 11 # Channel 3#4 run DC diag
d 300 #delay 300ms and read 0x72 and 0x73 register to confirm DC diag finish
r C0 72 01 # read channel 1#2 state till channels are Sleep mode.
r C0 73 01 # read channel 1#2 state till channels are Sleep mode.
r C0 C0 01 # read channel 1#2 DC diag result.
r C0 C1 01 # read channel 3#4 DC diag result.
## Set Channels to Hi-Z state ##
w C0 03 33 # Set Channel 1#2 to Hi-Z state
w C0 04 33 # Set Channel 3#4 to Hi-Z state

## Slide 5: Initiation of pilot tone and RTLDG
w C0 00 00 # Page switching (1st 00) to page 0 (2nd 00)
w C0 7F 00 # Change to book 0. It's required to be in page 0 before
### Enable Current Sense ###
w C0 D0 00 # RTLDG off
w C0 05 0F # Enable Current Sense on all 4 channels
w C0 5B 08 # Optimize for 4 x BTL configuration, leave RTLDG report disabled
w C0 5C 40 # Optimize for 4 x BTL configuration
w c0 39 01 # Turn off DC blocking
w C0 03 44 # # Set Channel 1#2 to play state
w C0 04 44 # # Set Channel 3#4 to play state
### Enable pilot tone ###
w C0 00 00 # Page switching (1st 00) to page 0 (2nd 00)
w C0 7F 8C # Change to book 8C. It's required to be in page 0 before changing a book
w C0 00 03 # Go to the page 03 in book 8C
w C0 48 00 00 00 00 # 32-bit value: 0x0 = Enable; 0x1 = Disable
w C0 00 00 # Page switching (1st 00) to page 0 (2nd 00)
w C0 7F 78 # Change to book 78. It's required to be in page 0 before changing a book
w C0 00 19 # Go to the page 19 in book 78
w C0 3C 10 00 00 00 # Write to offset 3C, 32-bit wide, to set Re init value
w C0 48 10 00 00 00 # Write to offset 48, 32-bit wide, to set Re init value
### Set Thresholds for OL and SL ###
w C0 00 00 # Return to page 0 of book 78
w C0 7F 8C # Change to book 8C. It's required to be in page 0 before changing a book
w C0 00 02 # Go to the page 02 in book 8C
w C0 88 1D 00 00 00 # Write to offset 88, 32-bit wide, set Open load threshold e.g. ~40ohm
w C0 8C 00 C5 00 00 # Write to offset 8C, 32-bit wide, set Short load threshold e.g. ~1ohm
### Set Thresholds for S2P and S2G ###
w C0 00 04 # Go to the page 04 in book 8C
w C0 58 00 00 00 01 # Enable S2P#S2G detection
w C0 64 04 2E D9 84 # Set S2P current threshold to ~1A (configurable)
w C0 00 05 # Go to the page 05 in book 8C
w C0 90 06 2E D9 84 # Set S2G current threshold to ~1.5A (configurable)
### Enable RTLDG ###
w C0 00 00 # Return to page 0 of book 8C
w C0 7F 00 # Return to book 0, page 0
w C0 5B 0A # Enable RTLDG Report, 4 x BTL configuration

## Slide 6: Disable RTLDG and clear fault – Slide #1
w C0 00 00 # Page switching (1st 00) to page 0 (2nd 00)
w C0 7F 00 # Change to book 0. It's required to be in page 0 before
w C0 5B 08 # Disable RTLDG report (4 x BTL configuration)
w C0 01 08 # Clear Fault
d 100 #delay 100ms
w C0 00 00 # Page switching (1st 00) to page 0 (2nd 00)
w C0 7F 00 # Change to book 0. It's required to be in page 0 before
w C0 03 44 # Set channels 1#2 to PLAY state
w C0 04 44 # Set channels 3#4 to PLAY state
d 100 #delay 100ms
### Release DSP buffer ###
w c0 00 00
w C0 7F 78 # Change to book 78. It's required to be in page 0 before changing a book
w C0 00 19 # Go to the page 19 in book 78
w C0 3C 10 00 00 00 # Write to offset 3C, 32-bit wide, to set Re init value
w C0 48 10 00 00 00 # Write to offset 48, 32-bit wide, to set Re init value
w c0 00 00
w c0 7f 78
w c0 00 04
w c0 58 00 00 00 00
w c0 5c 00 00 00 00
w c0 60 00 00 00 00
w c0 64 00 00 00 00
w c0 00 08
w c0 20 00 00 00 00
w c0 24 00 00 00 00
w c0 28 00 00 00 00
w c0 2c 00 00 00 00
w c0 30 00 00 00 00
w c0 34 00 00 00 00
w c0 38 00 00 00 00
w c0 3c 00 00 00 00
w c0 40 00 00 00 00
w c0 44 00 00 00 00
w c0 48 00 00 00 00
w c0 4c 00 00 00 00
w c0 50 00 00 00 00
w c0 54 00 00 00 00
w c0 58 00 00 00 00
w c0 5c 00 00 00 00
w c0 60 00 00 00 00
w c0 64 00 00 00 00
w c0 68 00 00 00 00
w c0 6c 00 00 00 00
w c0 70 00 00 00 00
w c0 74 00 00 00 00
w c0 78 00 00 00 00
w c0 7c 00 00 00 00
w c0 80 00 00 00 00
w c0 84 00 00 00 00
w c0 88 00 00 00 00
w c0 8c 00 00 00 00
w c0 90 00 00 00 00
w c0 94 00 00 00 00
w c0 98 00 00 00 00
w c0 9c 00 00 00 00
w c0 a0 00 00 00 00
w c0 a4 00 00 00 00
w c0 a8 00 00 00 00
w c0 ac 00 00 00 00
w c0 b0 00 00 00 00
w c0 b4 00 00 00 00
w c0 b8 00 00 00 00
w c0 bc 00 00 00 00
w c0 c0 00 00 00 00
w c0 c4 00 00 00 00
w c0 c8 00 00 00 00
w c0 cc 00 00 00 00
w c0 d0 00 00 00 00
w c0 d4 00 00 00 00
w c0 d8 00 00 00 00
w c0 dc 00 00 00 00
w c0 e0 00 00 00 00
w c0 e4 00 00 00 00
w c0 e8 00 00 00 00
w c0 ec 00 00 00 00
w c0 f0 00 00 00 00
w c0 f4 00 00 00 00
w c0 f8 00 00 00 00
w c0 fc 00 00 00 00
w c0 00 09
w c0 10 00 00 00 00
w c0 14 00 00 00 00
w c0 18 00 00 00 00
w c0 1c 00 00 00 00
w c0 20 00 00 00 00
w c0 24 00 00 00 00
w c0 28 00 00 00 00
w c0 2c 00 00 00 00
w C0 00 10 #Move to page 16
w C0 78 00 00 00 00 #CH1 Pside offset current
w C0 7C 00 00 00 00 #CH2 Pside offset current
w C0 58 00 00 00 00 #CH1 Nside offset current
w C0 5C 00 00 00 00 #CH2 Nside offset current
Part #1
Part #2
Part #3

## Slide 7: Disable RTLDG and clear fault - Slide #2
d 500 #delay 500ms
### Release DSP buffer ###
w c0 00 00
w C0 7F 78 # Change to book 78. It's required to be in page 0 before changing a book
w C0 00 19 # Go to the page 19 in book 78
w C0 3C 10 00 00 00 # Write to offset 3C, 32-bit wide, to set Re init value
w C0 48 10 00 00 00 # Write to offset 48, 32-bit wide, to set Re init value
w c0 00 00
w c0 7f 78
w c0 00 04
w c0 58 00 00 00 00
w c0 5c 00 00 00 00
w c0 60 00 00 00 00
w c0 64 00 00 00 00
w c0 00 08
w c0 20 00 00 00 00
w c0 24 00 00 00 00
w c0 28 00 00 00 00
w c0 2c 00 00 00 00
w c0 30 00 00 00 00
w c0 34 00 00 00 00
w c0 38 00 00 00 00
w c0 3c 00 00 00 00
w c0 40 00 00 00 00
w c0 44 00 00 00 00
w c0 48 00 00 00 00
w c0 4c 00 00 00 00
w c0 50 00 00 00 00
w c0 54 00 00 00 00
w c0 58 00 00 00 00
w c0 5c 00 00 00 00
w c0 60 00 00 00 00
w c0 64 00 00 00 00
w c0 68 00 00 00 00
w c0 6c 00 00 00 00
w c0 70 00 00 00 00
w c0 74 00 00 00 00
w c0 78 00 00 00 00
w c0 7c 00 00 00 00
w c0 80 00 00 00 00
w c0 84 00 00 00 00
w c0 88 00 00 00 00
w c0 8c 00 00 00 00
w c0 90 00 00 00 00
w c0 94 00 00 00 00
w c0 98 00 00 00 00
w c0 9c 00 00 00 00
w c0 a0 00 00 00 00
w c0 a4 00 00 00 00
w c0 a8 00 00 00 00
w c0 ac 00 00 00 00
w c0 b0 00 00 00 00
w c0 b4 00 00 00 00
w c0 b8 00 00 00 00
w c0 bc 00 00 00 00
w c0 c0 00 00 00 00
w c0 c4 00 00 00 00
w c0 c8 00 00 00 00
w c0 cc 00 00 00 00
w c0 d0 00 00 00 00
w c0 d4 00 00 00 00
w c0 d8 00 00 00 00
w c0 dc 00 00 00 00
w c0 e0 00 00 00 00
w c0 e4 00 00 00 00
w c0 e8 00 00 00 00
w c0 ec 00 00 00 00
w c0 f0 00 00 00 00
w c0 f4 00 00 00 00
w c0 f8 00 00 00 00
w c0 fc 00 00 00 00
w c0 00 09
w c0 10 00 00 00 00
w c0 14 00 00 00 00
w c0 18 00 00 00 00
w c0 1c 00 00 00 00
w c0 20 00 00 00 00
w c0 24 00 00 00 00
w c0 28 00 00 00 00
w c0 2c 00 00 00 00
w C0 00 10 #Move to page 16
w C0 78 00 00 00 00 #CH1 Pside offset current
w C0 7C 00 00 00 00 #CH2 Pside offset current
w C0 58 00 00 00 00 #CH1 Nside offset current
w C0 5C 00 00 00 00 #CH2 Nside offset current
d 500 #delay 500ms
w C0 00 00 # Return to page 0 of book 8C
w C0 7F 00 # Return to book 0, page 0
w C0 5B 0A # Enable RTLDG Report, 4 x BTL configuration
Part #4
Part #5