## Slide 1
Customer is using TLV320AIC3101 for several years.
Recently, there have issue ( stuck no output ) in case fs change.
Customer is investigating the cause now , but
Customer is not fully confident with their procedure...
Inquiry
1)
Please kindly check Customer’s procedure in their products which is in page 2.
Is there any criteria to keep other than page2 ~ 3?
Do you have any problem in customer's procedure?
Would you please advise your recommended procedure (Do and Don’ts)
in order to change fs (48K~96K) ?

## Slide 2
DAC MUTE
ADC MUTE
DAC Power Down
ADC Power Down
Set PLL Disable
Set PLL Settings (Note2)
Set I2S Master Mode
PLL Enable
_codec Power Disable
_setSampleRate
Wait 11msec for PLL stability
ADC Power Up
DAC Power Up
ADC unmute
DAC unmute
_codec Power Enable
Set I2S SLAVE MODE( Note1)
MCLK
Input
From X’tal
To AIC3101
BCLK/WCLK
Output
from AIC3101
To DSP
12.0000
MHz
BCK 3.072MHz
/ WCLK 48KHz
12.000
MHz
6.144
MHz
/ 96KHz
C55x
AIC
3101
MCLK
12.000
MHz
BCLK(64fs)
WCLK
DOUT
DIN
Fig 1 Fs change procedure
( ex. 48K to 96KHz)
MCLK(X’tal)
Supplied
continuously
BCK/WCLK
Stopps
X’tal
I2C (MCU)
Power down /up
recommended
In slaa230a.pdf
Note1
As per customer, to set slave mode is necessary for
Disabling PLL in order to stop WCLK, BCK.
As per customer, ADC/DAC power down/up,
to stop WCLK/BCK at once, change PLL setting is the
best way for Fs change, but it is by their cut&try,not authorized.
( I personally have no idea the reason why set slave mode at once in order to disable PLL and change PLL setting in master mode )
Note2
Pls refer PLL setting detail in the next page .( for 96KHz, same PLL setting but double rate)
Fig2 Block diagram

## Slide 3
PLL setting detail
1) In case 44.1K/48K: Follow table2 and discription in data sheet p23
In case 96K
Set dual rate mode. ( Pother setting ;R,J,D is same as 48KHz case)