## Slide 1
DAC MUTE
ADC MUTE
DAC Power Down
ADC Power Down
Set PLL Disable
Add Wait
Set PLL Settings (Note2)
Set I2S Master Mode
PLL Enable
_codec Power Disable
_setSampleRate
Wait 11msec for PLL stability
ADC Power Up
DAC Power Up
ADC unmute
DAC unmute
_codec Power Enable
Set I2S SLAVE MODE( Note1)
MCLK
Input
From X’tal
To AIC3101
BCLK/WCLK
Output
from AIC3101
To DSP
12.0000
MHz
BCK 3.072MHz
/ WCLK 48KHz
12.000
MHz
6.144
MHz
/ 96KHz
C55x
AIC
3101
MCLK
12.000
MHz
BCLK(64fs)
WCLK
DOUT
DIN
Fig 1 Fs change procedure
( ex. 48K to 96KHz)
MCLK(X’tal)
Supplied
continuously
BCK/WCLK
Stopps
X’tal
I2C (MCU)
Power down /up
recommended
In slaa230a.pdf
Note1
As per customer, to set slave mode is necessary for
Disabling PLL in order to stop WCLK, BCK.
As per customer, ADC/DAC power down/up,
to stop WCLK/BCK at once, change PLL setting is the
best way for Fs change, but it is by their cut & try..
( I personally I have no idea the reason why necessary to set slave mode
at once in order to disable PLL and change PLL setting in master mode )
Note2
Pls refer PLL setting detail in the next page .( for 96KHz, same PLL setting but double rate)
Fig2 Block diagram
Is it no problem?