## Slide 1: Clocking High Speed Data Converters
High Speed Data Converters

## Slide 2: Presentation Goals
Understand the theory behind the relationship between SNR, noise sources, ADC performance
Know how to select the appropriate clocking solution for a given application
Learn about additional techniques for improving sampling clock quality to the ADC
Understand the clocking effects of DACs and the tradeoffs between jitter and NSD specifications
Become familiar with TI’s clocking solutions portfolio

## Slide 3: UnderstandING the theory for adcS
SNR, Noise Sources, and ADC Performance

## Slide 4: Signal-to-Noise Ratio Basics
Noise Signal Noisy Signal
FREQUENCY (Hz)
Signal
Noise Level
In the time domain:
In the frequency domain:
FFT
SNR is the ratio of the signal power to the noise power that corrupts the signal. This parameter does not include harmonic distortion.

## Slide 5: Maximizing the SNR in an ADC
SNR can be increased in the following ways:
Increase signal power ↑
  Full Scale Range (FSR)
Decrease noise power ↓
  Quantization Noise
  Clock Jitter
  ADC Aperture Jitter
  Thermal Noise
Thermal
Clock Jitter
Aperture Jitter
Quantization

## Slide 6: SNR by Individual Contributors
Total SNR can be calculated by the sum of the individual sources:
Design Choice | Effect on Noise
ADC Selection | N-bits affects quantization noise, aperture jitter and thermal noise by design
Sampling Clock Selection | Clock jitter
Sampling Rate | Bandwidth over which noise is distributed
SNRQUANT = SNR due to quantization
SNRJITTER = SNR due to clock and aperture jitter
SNRTHERM = SNR due to thermal and transistor noise

## Slide 7: Quantization Noise and SNR
SNR due to quantization error, assuming a sine wave input:
How to determine the required ADC resolution?
  An N-bit ADC determines the maximum possible SNR for the system
  Practically, an ADC’s SNR is limited by other factors:
    Sampling clock jitter
    ADC jitter and thermal noise
    Other system noise sources
    Over-sampling rate and application channel bandwidth
Example: 14-bit converter where N=14:

## Slide 8: Transistor and Thermal Noise and SNR
Noise Mechanism | α | Spectral Profile | Source | Cause
Shot | IDC | white | pn-junctions | DC bias current is not constant
Flicker | 1/f | 1/f | Active devices | Carriers are “trapped” and released in a semiconductor
Thermal | T | white | resistors | Thermal excitation of carriers in a conductor
Noise in an ADC:
Track-and-hold is dominant source
Capacitors source no noise
Resistor results in “kT/C” noise
Notes: Noise bandwidth is given by (pi*2)/f
f = 1/(2*pi*RC) due to white spectral density

## Slide 9: Clock Jitter and SNR
Clock jitter is the random variation of the clock edge compared to its ideal point in time
Theoretical limit of SNR due to jitter:
Total jitter is the rms sum of the individual jitter contributions
  For ADCs, this is generally the external clock jitter and aperture jitter

## Slide 10: More on Clock Jitter
Clock jitter causes imprecise sampling intervals which results in incorrect sampling instances and therefore errors in the sampled signal
Clock jitter has an increased effect at higher input frequencies or higher maximum input slew rates

## Slide 11: Sources of Clock Jitter
The total clock jitter for an ADC is from the aperture jitter and the external sampling clock jitter.
Clock jitter is the jitter contribution from the external clock source and can be measured by using a phase noise analyzer
Aperture jitter (a.k.a. aperture uncertainty) is the jitter contribution from the ADC, due to the internal clock buffers. This cannot be measured directly using a phase noise analyzer.
Example: aperture jitter for the ADS4249
The total clock jitter is determined by rms sum of all individual contributions:

## Slide 12: Example Phase Noise Plot
Noise Spectral Density (dBc/Hz)
Frequency (MHz)

## Slide 13: Calculating Jitter from Clock Phase Noise
Jitter is a result of noise on the sampling clock. Assuming the wideband clock noise is relatively low, then the clock jitter is calculated by integrating the clock phase noise over a specified BW then converting to seconds.
Example from previous slide’s phase noise plot:
  FN = -75.72 dBc/Hz (from 10 kHz to 10 MHz offset)
  Fclk = 122.88 MHz
  Where:
  FN= Phase Noise Power (dBc)
  f0, f1= frequency limits of integration
  tj = clock jitter

## Slide 14: SELECTING an ADC CLOCK

## Slide 15: Determining Clock Jitter Requirements
The target SNR is generally based on the system requirements
Then ADC aperture jitter and IF center frequency can be used to calculate the required external clock jitter performance
Use Jitter Calculator Worksheet:
  http://www.ti.com/litv/zip/slac133
  The current worksheet does not account for the contribution from quantization and thermal noise (see total SNR from earlier)

## Slide 16: Example: ADS5483 (16-bit, 125 MSPS)
Aperture jitter: tj = 80 fs
Input Frequency: fIN = {10 MHz, 100 MHz}
SNR from datasheet:
  Includes effect of thermal and quantization noise, and aperture jitter
  External clock jitter is negligible since the highest quality source was used
Clock source:
  LMK04803 with 80 MHz VCXO in dual-loop mode
  10 MHz reference from analog input signal generator
  125 MHz LC bandpass filter on clock signal
  Phase noise plot on next screen

## Slide 17: Example: ADS5483 – Clock Phase Noise
114 fs of jitter in integration band of 1 kHz to 40 MHz

## Slide 18: Example: ADS5483 – SNR Analysis
10 MHz Case:
From datasheet:
  SNR @ 10 MHz = 79 dBFS
From spreadsheet:
Total estimated SNR:
100 MHz Case:
From datasheet:
  SNR @ 100 MHz = 78.2 dBFS
From spreadsheet
Total estimated SNR:
Assuming -1 dBFS Input
Assuming -1 dBFS Input

## Slide 19: Example: ADS5483 – 10 MHz FFT
Error: | 79.13 dBFS – 78.98 dBFS | = 0.15 dB

## Slide 20: Example: ADS5483 – 100 MHz FFT
Error: | 76.83 – 76.73 | = 0.10 dBFS

## Slide 21: Estimating NSD from SNR
The Noise Spectral Density can be approximated by using SNR from the datasheet at low input frequency:
Example: from ADS4249 Datasheet with Fs = 250MSPS and N=14:
Clock noise can also be included in the NSD calculation by using the total SNR shown previously. It may be beneficial to look at the shape of the clock noise when considered NSD.
Ideal NSD by Quantization Noise:
Actual NSD by SNR at low Fin:

## Slide 22: additional techniques
Improving the Sampling Clock Quality

## Slide 23: A note on clock filtering
Clock sources have wideband noise that will also contribute to the overall jitter of the clock
  This is can be important since ADCs often have very wide clock input bandwidths (up to ~ 2 GHz)
In order to eliminate the wideband noise of the clock source, a filter can be placed on the clock lines
  A bandpass filter is preferred, but a low pass filter could be acceptable
  The amount of filtering will vary based on the system requirements
  A tight passband will have more loss which could have additional problems
Note that filtering a square wave will produce a sine wave with a slower slew rate, this may hurt the jitter performance slightly
Filtering the clock can eliminate clock related spurs, especially those associated with different frequencies coupling in due to clock isolation

## Slide 24: Clocking with Sine Wave vs. Square Wave
A square wave clock (e.g. LVPECL) has a very high slew rate, but does not allow clock filtering as clock harmonics generate the high slew rate
Filtering the clock removes clock noise, but limits the slew rate
Harmonics
Clock
Noise
Frequency
Bandpass Filter
Frequency
Lower Noise
Slew Rate
Slew Rate

## Slide 25: Example: LMK04803 Filtering
The plot below has two phase noise measurements overlaid from the same LMK04803, but the slightly darker trace has a relatively tight LC band-pass filter on it.
Note that the overall jitter in the 1 kHz to 40 MHz bandwidth has actually degraded slightly for the filtered case due to a slower slew rate from filtering out the harmonics.
However, the wideband noise has gone from -163 dBc/Hz to -174 dBc/Hz. Integrated over 500 MHz, this will make a significant difference (~200 fs) and will easily overcome the added jitter due to a lower slew rate.
Higher in-band phase noise
Lower wide-band noise

## Slide 26: Example: ADS5483 w/ and w/o filtering
Without Filter
With Filter
Clocking with a sine wave can reduce clock related spurs.

## Slide 27: Clocking ADCs: Effect of Clock Slew Rate
The jitter generated by the ADC clock receiver is affected by the clock slew rate
Filtering the ADC clock will lower the clock slew rate by removing the harmonics
A slower slew rate causes the receiver to be more susceptible to variations in the zero crossing point
A faster clock slew rate lowers the jitter due to the receiver voltage noise
Receiver
noise
DV/Dt =
slew rate
Receiver Jitter ~ Receiver Noise * DV/Dt
Aperture
Jitter
Total Jitter ~
(Clock Jitter2 +
Receiver Jitter2 +
Aperture Jitter2)1/2
Clock
Jitter

## Slide 28: Phase noise for slower slew rate
For a clock that has ~9 dBm less power, jitter has been increased from 31.52 fs to 72.208 fs
6.11 dBm Clock:
-3.35 dBm Clock:

## Slide 29: A different Way to look at Clock Jitter/Noise
29

## Slide 30: Limitation of the Traditional SNR Calculation Due to Jitter
The traditional SNR due to jitter equation gives the SNR over the entire Nyquist band, with the jitter measured over a wide clock offset frequency
The equation is a function of the analog input frequency and jitter performance
If the ADC clock is already fine tuned to the best jitter performance, would the only option left to meet the stringent SNR performance is to adjust the input frequency?
If so, what is the point of over-sampling ADCs?

## Slide 31: General Equation for ADC SNR
It turns out the SNR equation is also a function of clock frequency as well. Recall the jitter equation:
If we substitute the jitter equation into the SNR equation, we would get the following:
The first term is the inherent integrated noise due to clock noise. The second term is a correction term. This is important to help us understand the performance of over-sampling. If over-sampling is used, the SNR can be improved

## Slide 32: Why is the general equation important?
The general equation is important because the traditional equation often simplifies the ADC clock noise floor as an uniform white noise.
In reality, the ADC clock usually has better noise behavior as the offset frequency increases, and also, the clock is often well filtered.
Simplified integrated clock noise
Actual phase noise

## Slide 33: System Requirement Implication
Most importantly, some of the stringent system requirements often are bandwidth specific. I.e. noise spec over a specific bandwidth.
For instance, when given a certain blocker signal, the traditional SNR calculation may overestimate the noise over the bandwidth of the wanted signal. This may make jitter specification of the clock impossible to achieve.

## Slide 34: Experiment Result
Clocking the ADC with a 250MHz tone + 10MHz noise ranging from 240MHz to 250MHz
(DAC5681 output)
ADS4149 at 250MSPS
Two inputs shown and overlaid: 10MHz and 100MHz

## Slide 35: ADC Test Result
20log(250/10) = 28dBc
20log(250/100) = 8dBc

## Slide 36: DAC NSD vs SNR
36

## Slide 37: SNR Jitter estimate is the same for DACs
The total SNR is the vector sum of all individual SNR contributions
Similar treatment of clock jitter (integrated phase noise) for SNR limit of DAC sampled system
37
SNRQUANT = SNR due to quantization
SNRCLK = SNR due to clock and aperture jitter
SNRTHERM = SNR due to thermal and transistor noise

## Slide 38: Is Jitter Applicable For DACs?
For DACs, generally the noise spectral density (NSD) is more important than overall SNR
  The shape of the NSD around the carrier must meet mask requirements
  When SNR is required, customer’s often limit the bandwidth of the transmitted signal by a bandpass or lowpass filter
For this reason, newer datasheets report NSD rather than SNR
fs = 1GSPS
f out = 20MHz
Noise
Signal
DAC output noise is comprised of
  Quantization noise
  Thermal noise
  Jitter noise
  Data dependent noise

## Slide 39: Why NSD over SNR?
In real systems, there is often tight filtering around the band of interest, where all the noise outside of that band is filtered out.
Rather than showing the SNR of the signal in the first Nyquist zone, it is more convenient to show the noise power so that the total noise power in the unfiltered band can be readily calculated
For example, consider a DAC3484 running at 1228.8 MSPS with a band of interest of 100 MHz and the following filters:
  A 614.4-MHz low-pass filter (passing full first Nyquist zone):
  A 100-MHz low-pass filter:
39

## Slide 40: Converting NSD to SNR
The SNR of the DAC can be calculated from the NSD spec
The SNR was traditionally defined as the ratio of the power of the fundamental to the power of the noise integrated over the first Nyquist zone.
It can also be calculated directly in dBFS from the NSD in dBc/Hz
Example: DAC3484 running at 1.25 GSPS with 10 MHz output
40

## Slide 41: NSD to SNR tradeoffs – Jitter/Phase noise
SNR estimates based on Jitter are good estimates for SNR for the entire Nyquist band – may be too pessimistic for BW limited applications.
SNR estimates based on NSD (typically measured at some MHz offset) do not account for close-in phase noise which could affect inband EVM
  Useful for out of band estimates like ACPR
  Also useful for transmit mask requirements
Using the clock NSD curve and BW limited noise calculations would be the ideal solution for in-band and out-of-band measurements.

## Slide 42: CLK Phase Noise effects on sampled systems
For both sampled systems of the ADC and DAC the CLK phase noise will be translated from the clock to the sampled outputs with the following relationship:
All in-band (%EVM, RX sensitivity) and out-of-band (ACPR, TX Mask) measurements can be based on the measured phase noise plot of the ADC and DAC clock source

## Slide 43: Intrinsic DAC noise effects
At higher frequency offsets where the phase noise of the clock drops off, the intrinsic noise of the DAC will play a role in the overall noise floor of the output spectrum
Measurements of the CLK NSD and the DAC output NSD show that there is some discrepancy between the estimates – this is accounted for by the DAC intrinsic noise due to the Thermal/Device effects

## Slide 44: Intrinsic DAC noise effects
The Intrinsic DAC noise is frequency dependent and measured at a particular offset frequency will only be approximately accurate for other offset frequencies.
Intrinsic Noise estimates made at 40MHz offset are somewhat accurate for NSD estimates at the same frequency offset using different clock sources.
The intrinsic noise is due to quantization and thermal noise sources
DAC intrinsic noise @40MHz
-162
-160
-158
-156
-154
-152
-150
-148
-146
0
50
100
150
200
250
300
350
400
450
500
DAC output frequency
DAC noise
Error in all cases
-2
-1.5
-1
-0.5
0
0.5
1
1.5
2
0
50
100
150
200
250
300
350
400
450
500
DAC output frequency (MHz)
Error (dB)
1ps_peaking
500fs_peaking
200fs_peaking
1ps_1MHz
500fs_1MHz
200fs_1MHz

## Slide 45: Examples using NSD for %EVM and ACPR
45

## Slide 46: DAC NSD Application measurement - EVM
WCDMA signal 3.84MHz BW, IF=122.88M, Sample rate 983.04Msps, 1% EVM
Assuming that %EVM is a measure of the SNR of the average inband signal power to the average inband NSD we can estimate the required average NSD of the clock (-105.84dBc/Hz avg at DAC output)
Scale by IF and Sample rate (-87.78dBc/Hz avg at Clock source)

## Slide 47: DAC NSD Application measurement - EVM
Average Clock NSD within 3.84MHz around the fundamental clock frequency needs to be less than -87.78dBc/Hz
The average clock NSD must be less than the predicted clock NSD to meet system requirements for EVM
Predicted clock NSD
Peaking NSD – cause EVM fluctuation
1.92MHz
Average in-band NSD @ clock – determine EVM
Phase noise
Frequency shift

## Slide 48: DAC NSD Application measurement - ACPR
WCDMA signal 3.84MHz BW, IF=122.88M, Sample rate 983.04Msps, ACPR=70dB, Alt ACPR=75dBc
The Clock NSD for both the ACPR and Alt ACPR is given by:
Clock NSD ACPR = -118dBc/Hz, Clock NSD Alt ACPR = -123dBc/Hz

## Slide 49: DAC NSD Application measurement - ACPR
Using some common clock sources we can see that the Clock NSD at ACPR and Alt ACPR frequency offsets is well below these NSD numbers.
Phase noise performance
-160.00
-140.00
-120.00
-100.00
-80.00
-60.00
1.00E+02
1.00E+03
1.00E+04
1.00E+05
1.00E+06
1.00E+07
1.00E+08
Phase noise
1ps_close_in
1ps_peaking
500fs_close_in
500fs_peaking
200fs_peaking
200fs_wide_band

## Slide 50: DAC NSD Application measurement - ACPR
Clock NSD at the ACPR and Alt ACPR offsets that there is negligible difference between using different clocks at different IF frequencies. Follows the shape of Intrinsic DAC noise.

## Slide 51: DAC NSD Application measurement – Alt ACPR
Same results with Alt ACPR.