## Slide 1: Configuration Planning

## Slide 2: DAC38J84 Example Configuration
Input data
    5M Wideband carrier at 30MHz Complex IF
    Input Digital Data rate = 737.28Msps
DAC settings:
    2X interpolation – DAC output rate 1474.56 Msps
    NCO setting at 150M – output IF at 180MHz
LMFS Calculation
    LMFS=8411
      Use L=8 lanes, M=4 Converters, F=1 Octet per frame, K=20, S=1 Sample per converter per frame
LMFC = Fs/(S*K) = 36.864Msps
SYSREF = LMFC/n = 36.864Msps max (n=1)
Lane rate = ???

## Slide 3: How is the DAC LMF chosen?
DAC38J84: 16b Quad DAC with up to 8 lanes JESD204B up to 12.5Gbps/lane
Data rate = 737.28Msps/DAC, 4 DACs = M = 4
Octet rate per DAC: 2 octets (16 bits) per sample
    737.28Msps*2 = 1474.56Moctets/sample/DAC
Bitrate per DAC: 8b/10b coding
    1474.56Moctets/s*10bits/octet = 14,745.6Mbps
Total bit rate = 4 DACs * 14.7456 Gbps = 58.9824Gbps (total through put)
If we choose L=8 lanes then the lanerate:
    Lane rate = 58.9824Gbps/8 = 7.3728 Gbps per lane
LMFS=8411, lane rate = 7.3728Gbps