## Slide 1: DAC38J84 100MHz NCO test

## Slide 2: Hardware Setup
DAC38J84
  Connect output SMA J2 (channel A) to Spectrum Analyzer
  Connect USB cable to J14 and host PC
  Connect the provided +5VDC power supply to J6 (located on bottom)

## Slide 3: Quick Start settings

## Slide 4: Go to “DAC3XJ8X Controls” tab. Set Input Data Format to “Offset Binary”. Enable “Const Input”.

## Slide 5: Go to “Dig Block1” tab. Enable “Mixer Block EN” and “NCO Enable”.

## Slide 6: Enter NCO frequency. Enter DAC clock frequency. Click on “Perform SIF SYNC”.

## Slide 7: 100MHz CW output will now appear at DAC output