## Slide 1: ADC32RF45 Testing

## Slide 2
ADC32RF45, TSW14J10, VC707 Setup

## Slide 3
Test Setup:
Single tone is given as input to the device.
Test conditions:
Fs = external 2.2GHz
Fin = 600MHz
LMK = 2.2GHz, clock dist mode
Mode = 8224, 14 bit
Ref clock = 550MHz
Core clock = 275MHz

## Slide 4: Load the following Quick Setup tab settings and click on “Program EVM”

## Slide 5: Click on Clock Outputs tab. Set CLKout 0 divider to 4 Enable CLKout 12. Set the divider to 8, and DCLK type to LVDS

## Slide 6: Open HSDCD Pro, select: “ADC32RF45_LMF_8224” Enter “2.2G” for ADC Output Data Rate

## Slide 7
Capture results using a 600MHz input tone