## Slide 1: ADS52J91 TSW14J56 to TSW14J50 transition
Texas Instruments
Feb 2023

## Slide 2: Comparison: TSW14J50 vs TSW14J56
Feature | TSW14J56 | TSW14J50
JESD204B support | Subclass 0, 1, 2 | Subclass 0, 1
Max lane rate | 12.5 Gbps | 6.5 Gbps
Availability | Not available | Available
Note:
Max lane rate supported by TSW14J50 is 6.5 Gbps.
JESD204B Subclass 2 is not supported by TSW14J50
So, some ADS52J91 EVM configurations are not supported by TSW14J50. The user is advised to evaluate the ADS52J91 EVM within these constraints.

## Slide 3: Installation
Download ‘High Speed Data Converter Pro - Installer v4.9’ from the ADS52J65 folder in My Secure Share (or TI Drive)
  Install HSDC Pro
Download ‘Setup_ADS52J91_EVM_v1.0.0.exe’ from the ADS52J91 folder in My Secure Share (or TI Drive)
  Install ADS52J91_EVM_GUI
Restart the computer

## Slide 4: Installation
From the folder ‘ADS52J91_TSW14J50_transition’ shared on My Secure Share (or TI Drive)
  Unzip ‘TSW14J50_TSW14J50RX_FIRMWARE’ to ‘./TSW14J50_TSW14J50RX_FIRMWARE’ folder. Ensure that there are no subfolders inside the ‘TSW14J50_TSW14J50RX_FIRMWARE’ folder.
  Copy unzipped folder ‘TSW14J50_TSW14J50RX_FIRMWARE’ and paste in “C:\Program Files (x86)\Texas Instruments\ADS52J91 EVM\Config Files\ADS52J91\ADS52J91vA\Firmware INI Files”
  Unzip ‘TSW14J50’ to ‘./TSW14J50’ folder. Ensure that there are no subfolders inside the ‘TSW14J50’ folder.
  Copy unzipped folder ‘TSW14J50’ and paste in “C:\Program Files (x86)\Texas Instruments\ADS52J91 EVM\Config Files\ADS52J91\ADS52J91vA\Scripts\Quick Start\JESD”
  Copy file ‘ADS52J91vA_GUI’ and replace in path “C:\Program Files (x86)\Texas Instruments\ADS52J91 EVM\Config Files\ADS52J91\ADS52J91vA”
  Copy the configuration file ‘ADS52J91’ and paste in “C:\Program Files (x86)\Texas Instruments\High Speed Data Converter Pro\14J50 Details\ADC files”

## Slide 5: Capturing a Ramp with the JESD Interface

## Slide 6: EVM Hardware Setup
Board Mating: Mate the TSW14J50 EVM at connector J4 to the ADS52J91 EVM at connector J32 through the FPGA Mezzanine Card (FMC) connector.
Power Supply: Connect a 5-V (3-A) power supply using the provided power cable to J11 (+5V_IN) of the TSW14J50 EVM . See the TSW manual for more information, if needed.
Next, connect a 5-V (3-A) power supply using the provided power cable to J46 of the ADS52J91 EVM. Connect the white-striped side of this cable to the 5-V power supply.
USB: Connect the USB cable from PC to J45 (USB) located on the top side of the ADS52J91 EVM. Connect the USB cable from PC to J9 of the TSW14J50 EVM. USB 2.0 or 3.0 ports are both acceptable for both EVMs. Note: TI recommends that the PC USB port be able to support USB2.0. If unsure, always choose the USB ports at the back of the PC chassis over ones located on the front or sides.
Clock: Connect REF_CLK of 200 MHz of 1 Vpp swing to J75, LMK_CLK_IN

## Slide 7: EVM Hardware Setup
Figure 1. TSW14J50EVM and ADS52J91 EVM Hardware Setup for JESD Capture

## Slide 8: Software setup
Start HSDC Pro and chose ADS52J91 as shown below
  Click update the firmware. Ignore the warnings and proceed further.

## Slide 9: Software setup
Click DUT_RESET  then click Initialize Device
Select the below OUTPUT FORMAT and ADC FORMAT

## Slide 10: Software setup
Click ‘Capture’ button and then you must see a ramp waveform for JESD 4ADC/CH mode

## Slide 11: Software setup (Mode for SEL testing)
Click DUT_RESET  then click Initialize Device
Then load the config “C:\Program Files (x86)\Texas Instruments\ADS52J91 EVM\Config Files\ADS52J91\ADS52J91vA\Scripts\Quick Start\JESD\TSW14J50\LMK_CDM_MODE\16CH_MODE\ADS52J91_16ch_SINE_8L_16x_12b_GBLCLKDIV1_FSDIV2_SYSREFDIV20_20x.cfg” file by clicking the circled Folder tab
Set Ramp Pattern and fsamp = 100MHz

## Slide 12: Software setup
Click ‘Capture’ button and then you must see a ramp waveform for JESD 2ADC/CH mode