## Slide 1: DAC38RF82EVM bring up guide
6144 MSPS, Fully onboard clocking, with TSW14J56/57EVM

## Slide 2: DAC38RF82 EVM Overview
DAC38RFxx
(under heatsink)
5V input
Channel A
Channel B
External CLK
JP10 shorted means LMK_CLKin1 is sourced from the External CLK input divided-by-4 (through an onboard RF divider)
JP10
LMK_CLKin1
USB input
JP3

## Slide 3: DAC38RF82EVM setup details
Shunt JP3 shorted
Shunt JP10 removed
DAC Sample rate: 6144 MSPS
6x Interpolation -> DAC Input data rate = 1024 MSPS
LMK PLL2 set to VCO1 at 3072 MHz. DAC CLK divider set as 12 to provide 3072 MHz / 12 = 256 MHz tone for the DAC PLL reference.
DAC PLL, M=6, N=1 -> DAC CLK = 256MHz * 4 * (6/1) = 6144 MHz

## Slide 4: DAC38RF82EVM configuration
1.
Toggle reset
Wait until red
Toggle again
2. Press Load Default

## Slide 5: DAC38RF82EVM configuration
If you see this message, ignore it and press OK.
This is because in this default mode, the DAC is expecting a PLL reference input through SMA connector J4.

## Slide 6: DAC38RF82EVM configuration
Change these parameters for desired DAC configuration
Then press Configure DAC

## Slide 7: DAC38RF82EVM configuration
Uncheck CP Tri-state
Choose VCO1
Change R Divider to 6
Change N Divider to 74
Change Pre-scalar to 2
Press up arrow to change N Divider to 75 (software bug)
Verify that LMK LOCK and PLL2 LOCK Green LEDs are lit up on DAC EVM

## Slide 8: DAC38RF82EVM configuration
Change these parameters to 12 and set DCLK source to Divider

## Slide 9: DAC38RF82EVM configuration
1. PLL AUTO TUNE

## Slide 10: DAC38RF82EVM configuration
Press check LF Voltage
PLL LF Voltage should read as 4
** If PLL LF Voltage is not 4:
Toggle to DACCLK, then immediately toggle back to PLL Clock
PLL AUTO TUNE

## Slide 11: DAC38RF82EVM configuration
** If PLL LF Voltage is not 4:
Toggle to DACCLK, then immediately toggle back to PLL Clock
PLL AUTO TUNE

## Slide 12: DAC38RF82EVM configuration
** If PLL LF Voltage is not 4:
Toggle to DACCLK, then immediately toggle back to PLL Clock
PLL AUTO TUNE

## Slide 13: DAC38RF82EVM configuration
Press check LF Voltage
PLL LF Voltage should now read as 4

## Slide 14: DAC38RF82EVM configuration
Press send in HSDC Pro

## Slide 15: DAC38RF82EVM configuration
Press Reset DAC JESD Core & SYSREF TRIGGER

## Slide 16: DAC38RF82EVM configuration
Enable the NCO and set to 512 MHz (1.024G / 2)
Press Update NCO
Tones should appear on output at 112M, 312M, 912M

## Slide 17: DAC38RF82EVM configuration
Frequencies are not exact because spectrum analyzer is not reference locked to the DAC.
To fix this, reference lock signal generator to spectrum analyzer using 10MHz reference, apply a 122.88MHz input into J4, uncheck PLL1 tri-state, change N divider in PLL1 to match Clkin1 R divider value.