## Slide 1: TSW40RF82EVM/TSW14J56EVM Pattern File Triggering
08172018

## Slide 2: TSW40RF82EVM Config
Load “2T2R_RevC_ConstInput_6xDec_12xInt_2949p12M_5898p2_4915p2Gb.cfg”
Connect J3 to J9 in order
To connect the output of the
DAC to the input of the ADC.

## Slide 3: Files
Place the included ADC ini file in the directory
C:\Program Files (x86)\Texas Instruments\High Speed Data Converter Pro\14J56revD Details\ADC files
Place the included DAC ini file in the directory
C:\Program Files (x86)\Texas Instruments\High Speed Data Converter Pro\14J56revD Details\DAC files

## Slide 4: Trigger Setup
Connect J12 and J13 on TSW14J56EVM.
Enable Trigger Mode on ADC tab

## Slide 5: DAC Pattern File
Load the included pattern file. Note that the 5th column is controlling the behavior of the trigger. This column isn’t “seen” in HSDC Pro.

## Slide 6: DAC

## Slide 7: ADC
Click Read DDR Memory on ADC tab, and captured data will be plotted.