## Slide 1: JESD204B Subclass Overview

## Slide 2: www.ti.com, select data converters, then High Speed ADC, then JESD204B Interface

## Slide 3: Original Spec
TI Information – NDA Required
Defines a single lane high speed serial link connected to single/multiple
data converters with speed up to 3.125Gbps.
JESD204 – April 2006

## Slide 4: REVISIONS
Revision A extends the support to multiple aligned lanes with multipoint link. Maximum supported speed is the same, 3.15Gbps.
JESD204A – April 2008
TI Information – NDA Required

## Slide 5
TI Information – NDA Required
Subclasses: 0 (backward compatible), 1, 2
Support for Deterministic Latency
Frame clock changed to device clock
Serial lanes speeds up to 12.5Gb/s
JESD204B – July 2011
Notes: 0.5

## Slide 6: Deterministic Latency: Achieved
JESD204B achieves deterministic latency: known/constant latency
  Subclass 0: DL not achieved (JESD204A)
  Subclass 1: DL achieved using SYSREF with strict timing
  Subclass 2: DL achieved using SYNC~ with strict timing
Deterministic Latency achieved with these architecture features
  SYSREF or SYNC~ are used to provide a deterministic reference phase to all devices for synchronization
  LMFC provides a low frequency reference to avoid frame clock phase ambiguity in the presence of link delay changes
  RX has an “elastic buffer” that absorbs link delay variation
Texas Instruments recommends/supports subclass 1
  LMFC phase easier to control with source synchronous SYSREF than with system synchronous SYNC~
Notes: 1

## Slide 7: Subclass 0, 1, 2
Three device subclasses have been defined. Each subclass uses a different link synchronization method.
  Subclass 0: Deterministic latency not supported. Backward compatible with JESD204A. No defined method for aligning local multi-frame clocks. Uses SYNC~ signal.
  Subclass 1: Deterministic latency is supported. Uses SYSREF clock to align local multi-frame clocks to device clocks in both TX and RX devices. May use SYNC~ signal to initiate a lane alignment sequence.
  Subclass 2: Deterministic latency supported. Uses SYNC~ to align local multi-frame clocks.

## Slide 8: JES204B Subclasses: 0
TI Information – NDA Required
Backward compatible with JESD204A but supports high line rates
No support for deterministic (known/constant) latency
Supports alignment of multiple lanes/device
Multi-device synchronization requires strict frame clock frequency and tight SYNC~ setup/hold timing
SYNC~ of subclass 0 has special timing requirements for error reporting
Mixing subclass 0 with subclass 1, 2 devices requires special SYNC~ error reporting considerations
Notes: 1

## Slide 9: JES204B Subclasses: 0
TI Information – NDA Required
SYNC~
TX device
RX device
Clock
Source
Frame Clock
Frame Clock
Data
Critical Timing Path for: Synchronization
Notes: 0.5

## Slide 10: JES204B Subclasses: 1
TI Information – NDA Required
Each device has an internal frame and local multi-frame clock
  Frame clock achieves serial transfer of symbols
  Local multi-frame clock (LMFC) achieves known latency
Requires the SYSREF signal
  SYSREF must be source synchronous with the device clock (critical)
  Phase of SYSREF events determine frame clock and local multi-frame clock alignments
Deterministic latency achieved
Supports alignment of multiple lanes/device
Multi-device synchronization achieved with close attention to device clock and SYSREF distribution
SYNC~ used for synchronization but is not timing critical
Notes: 1

## Slide 11: Clocking Scheme - Subclass 1
TI Information – NDA Required

## Slide 12: JES204B Subclasses: 2
TI Information – NDA Required
Each device has an internal frame and local multi-frame clock
  Same as subclass 1
SYNC~ signal used for synchronization and deterministic latency
  SYNC~ must be system synchronous with the device clock (critical)
  Phase of SYNC~ events determine frame clock and local multi-frame clock alignments
Deterministic latency achieved
Supports alignment of multiple lanes/device
Multi-device synchronization achieved with close attention to device clock and SYNC~ distribution
Since meeting setup and hold time becomes a challenge at higher sampling rates, it is recommended, as per standard, to use Subclass 1 for speeds above 500MSPS for both ADC and DAC.
Notes: 1

## Slide 13: Clocking Scheme – Subclass 2

## Slide 14: Summary
  JESD204: Standard serial data interface for data converters
  JESD204B subclasses offer 3 implementation variations
  Transport Layer defines data framing into serial lanes
  Link layer defines encoding, synchronization and data monitoring
  Physical layer defines the electrical and timing performance
  Deterministic latency achieved with subclasses 1, 2 and is required for known/constant latency through link
TI Information – NDA Required