## Slide 1: DAC38RF82 82380 Frame Format

## Slide 2: Transport Layer Parameters
Important parameters associated with transport layer include
  L # of lanes per converter device
  M # of converters per device
  F # of octets per frame (per lane)
  S # of samples per converter per frame clock cycle
  Hd High-Density bit which controls whether a sample may
  be divided over more lanes
  LMFS = 82380
Notes: 1

## Slide 3: Transport Layer Overview
This chart specifies how samples map to octets, lanes, etc
Notes: 1

## Slide 4
Highest Level
Lowest Level
Example of LMFSHd = 44840

## Slide 5: Transport Layer Example
Example: 11-bit octal ADC converter
L = 4, M = 8, F = 4, S = 1, CS = 2
Notes: 2

## Slide 6: Transport Layer Example
Example: 12-bit Dual DAC38RF82
L = 8, M = 2, F = 3, S = 8, Hd = 0
Notes: 2

## Slide 7: Transport Layer Example L = 8, M = 2, F = 3, S = 8, Hd = 0
Below 12-bit Dual DAC38RF82 example is only showing Lane 0 and Lane 1 data
CH1 will contain I data, and CH2 will contain Q data
S0 = sample 0, S1 = sample 1, ect…
Lane 0 = CH1 S0 bits [11:4], CH1 S0 bits [3:0], CH1 S1 bits [11:8], CH1 S1 bits [7:0]
F1
F2
F3
F1
F2
F3
Lane 1 = CH1 S2 bits [11:4], CH1 S2 bits [3:0], CH1 S3 bits [11:8], CH1 S3 bits [7:0]
1 Frame with 8 samples ( only 4 samples are shown. The other 4 samples will be on Lanes 2 and 3)
With F = 3, there will be three octets per Frame
S
Notes: 2

## Slide 8
With F = 3, there will be three octets per lane per Frame. Each octet is 8 bits unencoded or 10 bits encoded (8b/10b).
With S = 8, there will be 8 samples of data per channel per Frame.
Notes: 2