## Slide 1: LMK04828 Fundamentals
Chase Wood
Applications Engineer, High Speed Data Converters
October 17, 2022

## Slide 2: Typical clocking approaches
Highest performance
External clocking using low-noise signal generator:
  R&S SMA100B w/ B711 package (ultra low phase noise)
  Anritsu MG36221A w/ low phase noise package
LMX2820:
  Highest performance wideband clock synthesizer
  Supports output frequencies between 45MHz through 22.6GHz
LMX1204:
  Cleanest 1:4 clock distribution on market
  Allows for FPGA clock generation (logic_clk)
Highest flexibility/channels
LMK04828:
  Dual band VCO
    2370MHz – 2630MHz
    2920MHz – 3080MHz
  14 clock outputs
    7 data clock outputs
    7 SYSREF outputs
LMK04832 (-SP version available):
  Dual band VCO
    2440MHz – 2580MHz
    2945MHz – 3255MHz
  14 clock outputs
    Up to 14 data clock outputs
    Up to 7 SYSREF outputs

## Slide 3: LMK04828
Dual PLL
  PLL1 acts as jitter cleaner
  PLL2 locks the VCO frequency
Dual band VCO (voltage-controlled oscillator)
  2370MHz – 2630MHz
  2920MHz – 3080MHz
14 clock outputs
  7 data clock outputs
  7 SYSREF outputs
High flexibility device
LMK04828 is primary FPGA clock generation/distribution across JESD EVMs
DCLKout0 = FPGA
DCLKout2 = ADC/DAC

## Slide 4: Typical GUI Appearance – PLL1 Configuration

## Slide 5: Typical GUI Appearance – PLL2 Configuration

## Slide 6: Typical GUI Appearance – SYSREF

## Slide 7: Typical GUI Appearance – Clock Outputs

## Slide 8: PLL Basics
Phase-Locked Loop (PLL)
3 main components:
  Phase Detector
  Loop Filter
  VCO
Purpose: Generate an output tone resistant to phase drift

## Slide 9: Conditions for locking a PLL
Two main conditions:
  Input frequency into the PFD (phase-frequency-detector) from both the input and the feedback (VCO) must match
  Phase variation between the input and the feedback paths must not vary beyond a user defined value (typically 3.7ns)
  Specific to the LMK048xx, the above two conditions must be held for DLD (digital-lock-detect) number of cycles before the PLL will lock (DLD is a user defined value)

## Slide 10: LMK04828 – PLL1
Referred to as jitter cleaner stage
Narrow-loop bandwidth:
  Typically between 10Hz and 200Hz
Useful for reference locking LMK outputs to external equipment (required for coherency)
The reference input clock is NOT the PLL2 reference frequency!
The PLL2 reference frequency is the VCXO – typically a 122.88MHz or 100MHz Crystek
122.88MHz Crystek

## Slide 11: LMK04828 – PLL1
3 inputs: CLKin0, CLKin1, CLKin2
CLKin1 is the MOST useful
R-divider (0-16383)
N-divider (0-16383)
Charge Pump (CP)
  PLL1 requires external loop filter components (footprint savings, not all customers use PLL1)

## Slide 12: LMK04828 – PLL2
Referred to as main PLL stage
Wide-loop bandwidth:
  Typically between 50kHz and 200kHz
Used for synthesizing output clock(s)
The PLL2 reference frequency is the VCXO – typically a 122.88MHz or 100MHz Crystek
    Contains 2 internal VCOs covering 2370MHz – 2630MHz and 2920MHz – 3080MHz
122.88MHz Crystek

## Slide 13: LMK04828 – PLL2
Dual band VCO
  2370MHz – 2630MHz
  2920MHz – 3080MHz
R-divider (0-4095)
N-divider (0-262143)
Charge Pump (CP)
  PLL2 has internal filter with option for external loop filter connection

## Slide 14: Additional PLL2 Configuration Options
Pre-scalar: (/2 through /8)
VCO frequency exceeds PLL input range
Optional (*2) to double VCXO reference frequency

## Slide 15
To divider stages
PLL1 Configuration Tab
PLL2 Configuration Tab

## Slide 16: PLL Summary
  Input frequency into the PFD (phase-frequency-detector) from both the input and the feedback (VCO) must match
  Phase variation between the input and the feedback paths must not vary beyond a user defined value (typically 3.7ns for LMK04828)

## Slide 17: LMK04828 – SYSREF
SYSREF is used for JESD204B Subclass 1 - deterministic latency spanning multiple devices
SYSREF can be:
  Supplied through CLKin0 input
  Generated via SYSREF divider
All 7 SYSREF outputs are the same
Can be continuous SYSREF or pulsed SYSREF (aka. Pulser modes)

## Slide 18: LMK04828 – Output dividers
Integer dividers (1 through 32)
Individually controlled per each DCLKoutX
LMK04832 supports many integer dividers (1 through 1023)
Also includes delays (however we typically do not touch these ever)
122.88MHz Crystek

## Slide 19
Clock Outputs Tab

## Slide 20: Operational modes
Dual-loop mode (PLL1 + PLL2)
Single-loop mode (PLL2)
Zero-delay mode (special case of dual-loop mode)
Distribution mode (Bypass both PLLs)

## Slide 21: Dual-Loop Mode
PLL1 used for jitter cleaning and locking VCXO to the reference input to achieve coherency
PLL2 synthesizes a frequency on VCO0 or VCO1
Output dividers are used to create ADC/DAC clock and FPGA reference clock

## Slide 22: Single-Loop Mode
PLL1 is bypassed by tri-stating the PFD (phase-frequency-detector)
PLL2 synthesizes a frequency on VCO0 or VCO1
Output dividers are used to create ADC/DAC clock and FPGA reference clock

## Slide 23: Nested Zero-Delay Mode
PLL1 is active and R and N dividers are set to 1 (zero-delay mode)
PLL2 synthesizes a frequency on VCO0 or VCO1
Essentially the same as dual-loop mode, but feedback into PLL1 PFD comes from DCLKout6/8 or SYSREF (and not the CLKin0/1/2 input)
  Makes it useful for synchronizing across multiple EVM’s quickly
Ensures that PLL2 VCXO input is deterministic in phase to the output clock/SYSREF/feedback mux
Output dividers are used to create deterministic ADC/DAC clock and FPGA reference clock

## Slide 24: Distribution Mode
PLL1 is bypassed by tri-stating the PFD (phase-frequency-detector)
PLL2 is bypassed by tri-stating the PFD (phase-frequency-detector)
Passes the CLKin1 input to the divider stage, allowing for division of signal generator
Output dividers are used to create deterministic ADC/DAC clock and FPGA reference clock

## Slide 25: Quiz
True or False:
The relationship between (VCO frequency), (phase-detector frequency), and (N-divider output frequency) is = . In other words, does

## Slide 26: Quiz
True or False:
The relationship between (VCO frequency), (phase-detector frequency), and (N-divider output frequency) is = . In other words, does

## Slide 27: Quiz
What is the VCO frequency in the below configuration? Which VCO supports this frequency?
VCO0 = 2370MHz – 2630MHz
VCO1 = 2920MHz – 3080MHz
122.88MHz

## Slide 28: Quiz
What is the VCO frequency in the below configuration? Which VCO supports this frequency?
VCO0 = 2370MHz – 2630MHz
VCO1 = 2920MHz – 3080MHz
2457.6 MHZ falls within VCO0 range
122.88MHz
2456.7MHz
1228.8MHz
122.88MHz
122.88MHz
122.88MHz

## Slide 29: Quiz
What is the VCO frequency in the below configuration? Which VCO supports this frequency?
VCO0 = 2370MHz – 2630MHz
VCO1 = 2920MHz – 3080MHz
80MHz
Same question as before, but with different OSCin frequency

## Slide 30: Quiz
What is the VCO frequency in the below configuration? Which VCO supports this frequency?
VCO0 = 2370MHz – 2630MHz
VCO1 = 2920MHz – 3080MHz
2880 MHZ falls into the VCO gap, must use External VCO
TRICKY QUESTION, the answer is neither VCO can support this frequency!
80MHz
160MHz
2880MHz
1440MHz
160MHz
160MHz

## Slide 31: Resources
https://training.ti.com/ti-precision-labs-clocks-and-timing-phase-lock-loop-fundamentals
https://www.ti.com/lit/an/slyt169/slyt169.pdf