Part number：ads7066IYBHR

Question Describe：The values of single-point continuous sampling ADC differ greatly

In the use of ADS7066 single point external fixed voltage continuous sampling, found a large difference in sampling values.  During the re-debugging, the ADS7066 register is configured to use 1.8V internal fixed voltage （VTEST_EN=1）in diagnostic mode for AIN6 in manual acquisition mode.  Found that the sample values are still wide.

The data captured by logic analyzer is as follows:

Finally, the adS7066 Partial driver code is attached ：

void initADS7066(void)

{

// (OPTIONAL) Provide additional delay time for power supply settling

delay_ms(50);

DBG_DIRECT("initADS7066 start");

// Initialize internal 'registerMap' array with device default settings

restoreRegisterDefaults();

DBG_DIRECT("restoreregister finish,,next start writesingle register");

// Clear BOR flag

writeSingleRegister(SYSTEM_STATUS_ADDRESS, SYSTEM_STATUS_BOR_MASK);

//		//Set GENERAL_CFG

writeSingleRegister(GENERAL_CFG_ADDRESS ,  GENERAL_CFG_REF_EN_INTERNAL_REF_ENABLED|GENERAL_CFG_CAL_CALIBRATE_ADC_OFFSET );

//		//DATA_CFG  -----output fixed0xA5A5&4-bit status flags are appended to ADC data.

writeSingleRegister(DATA_CFG_ADDRESS  ,  DATA_CFG_APPEND_STATUS_FOUR_BIT_CHID   );

//		//OSR_CFG -- Selects the oversampling ratio for ADC conversion result.

//		//writeSingleRegister(OSR_CFG_ADDRESS  ,  OSR_CFG_OSR_NO_AVERAGING);

//		//OPMODE_CFG --Selects the oscillator for internal timing generation.&Sampling speed control when using averaging filters.

//		//writeSingleRegister(OPMODE_CFG_ADDRESS , OPMODE_CFG_DEFAULT);

//		//PIN_CFG--Configure device channels AIN/GPIO [7:0] as analog inputs or GPIOs

writeSingleRegister (PIN_CFG_ADDRESS ,0xBF);

//		//GPIO_CFG  --Configure GPIO[7:0] as either digital inputs(0b) or digital outputs(1b).

writeSingleRegister(GPIO_CFG_ADDRESS  ,0xBF);

//		//GPIO_DRIVE_CFG--Configure digital outputs GPO[7:0] as open-drain (0b)or push-pull outputs(1b).

writeSingleRegister(GPO_DRIVE_CFG_ADDRESS   ,0xBF);

//		//GPO_OUTPUT_VALUE --

writeSingleRegister(GPO_OUTPUT_VALUE_ADDRESS ,GPO_OUTPUT_VALUE_DEFAULT  );

//		//GPI_VALUE

//

////		************startManualConversions(5)************************88

////				//SEQUENCE_CFG --set Manual sequence MODE or auto sequence MODE(AUTO_SEQ_CHSEL sure sequence)

////				 writeSingleRegister(SEQUENCE_CFG_ADDRESS , SEQUENCE_CFG_DEFAULT );

////				 //CHANNEL_CFG  --in manual mode,set channel ID

////				 writeSingleRegister(CHANNEL_SEL_ADDRESS   , CHANNEL_SEL_ADDRESS  );

//

writeSingleRegister (DIAGNOSTICS_KEY_ADDRESS ,DIAGNOSTICS_KEY_DIAG_KEY_REG_WR_ACCESS_ENABLED );

writeSingleRegister (BIT_WALK_ADDRESS ,BIT_WALK_DIAG_EN_MASK );

//		 //AUTO_SEQ_CH_SEL---in auto sequence mode ,set scanning ch

startManualConversions(6);

DBG_DIRECT("initADS7066 successed");

}

void startManualConversions(uint8_t channelID)

{

// Select manual mode

writeSingleRegister(SEQUENCE_CFG_ADDRESS, SEQUENCE_CFG_SEQ_MODE_MANUAL);

// Configure pin as analog input

setChannelAsAnalogInput(channelID);

// Select channel as MUX input

writeSingleRegister(CHANNEL_SEL_ADDRESS, channelID);

// Set nCS pin LOW, next rising edge will trigger start of conversion

setCS(LOW);

// Start conversion timer

//   startTimer();

algorithm_align_timer_start();

}

int32_t readData(uint8_t dataRx[])

{

// Array to store ADC conversion results

uint8_t dataTx[4] = { 0 };

uint8_t numberOfBytes = SPI_CRC_ENABLED ? 4 : 3;

// Start conversion

setCS(HIGH);

// Wait for conversion to complete

// IMPORTANT: This delay will need to be modified if averaging is enabled!

delay_us(2);

// NULL command

dataTx[0] = OPCODE_NULL;

dataTx[1] = OPCODE_NULL;

dataTx[2] = OPCODE_NULL;

if (SPI_CRC_ENABLED) { dataTx[3] = calculateCRC(&dataTx[0], 3, 0xFF); }

else { dataTx[3] = OPCODE_NULL; }

// Set the nCS pin LOW

setCS(LOW);

// Send all dataTx[] bytes on MOSI, and capture all MISO bytes in dataRx[]

int i;

for (i = 0; i < numberOfBytes; ++i)

{

dataRx[i] = spiSendReceiveByte(dataTx[i]);

DBG_DIRECT("dataRx[%d]=%d",i,dataRx[i]);

}

return signExtend(dataRx);

}