## Slide 1: AM64X : Reset Architecture
Anil, Swargam

## Slide 2
AM64X SOC Architecture
Why Reset ?
3. The different types of resets on AM64X
4. Reset types and Their impact on Boot sequences and memories
5. How different resets act in Isolation Vs Generic Mode?
6. How to debug when the SOC continuously Resets ?
Agenda

## Slide 3
AM64x SOC Architecture :
MAIN Domain : 2 A53 cores and
4 R5F cores , MAIN MMR, MAIN Peripheral set and MAIN PLL
MCU Domain : M4F core, MCU MMR, MCU Peripheral set and MCU PLL
Generic Mode : When a user configures M4F as a generic processor,
Then Reset is propagated through both the MAIN and MCU domains.
​Isolation Mode : When the user configures M4F core as a Safety Processor, Then the Reset is propagated through the only MAIN domain and not propagated through the MCU core.
AM64x
16nmFF
2MB Shared SRAM
Power
Manager
Debug
Firewall
System
Monitor
DMA
Timers
System Services
IPC
Secure Boot
DCC ESM ECC
Security Acceleration
Crypto: AES, 3DES, SHA, PKA, RNG,
MCU with FFI
Cortex M4F
16b DDR4/LPDDR4
w/ ECC
Application Cores
Arm®
Cortex A53
256KB L2$
Arm®
Cortex A53
Cortex M3
Hardware Security Module
256KB RAM
Diagnostic toolkit: ECC, ESM, BIST, DCC, CRC
GPIO
2x I2C
2x SPI
2x UART
PRU-ICSS-Gb
Industrial Ethernet
Supported Protocols: TSN, EtherCAT, PROFINET, EtherNet/IP, PROFIBUS, SERCOS 3 and more…
General Connectivity & IO
Memory/Flash
GPMC
OSPI
x1
MMC/SD
x2
High-speed interfaces
2-port Gb Ethernet
w/1588 & TSN
1x USB 3.1/2.0*
GPIO
SPI
x5
UART
x7
I2C
x4
CAN-FD
x2
Analog
ADC
x1
Control Peripherals
eQEP
x3
eCAP
x3
ePWM
x9
PRU-ICSS-Gb
Motor control / Industrial Ethernet
9x SigmaDelta decimation filters
3x abolute encoder interfaces
Supported encoders:
Hiperface DSL, EnDat 2.2, Tamagawa, BiSS C etc
Real-time Core
Arm®
Cortex R5F
128KB TCM
Arm®
Cortex R5F
Real-time Core
Arm®
Cortex R5F
128KB TCM
Arm®
Cortex R5F
FSI
x8
1x PCIe (1L) Gen2*
* PCIe and USB 3.0 share the same SERDES
128KB SRAM

## Slide 4
What is Reset?
A Reset refers to a mechanism or signal that allows the entire system or specific components within the SOC to be reset to a known initial state.
Why do we need to use Reset ?
Resetting an SOC ensures that all its components start in a known state.
If an SOC or any of its components encounter an error or malfunction, a reset can be initiated to bring the system back to a stable and known state. This can help resolve issues caused by software bugs, hardware faults, or other unexpected conditions.

## Slide 5
Types of Resets are available on AM64X ?
There are two types of Resets:
Warm reset
Power-on reset (POR).

## Slide 6
Reset Types and Their impact on boot sequences and memories

## Slide 7
How different resets act in Isolation Vs Generic Mode?

## Slide 8
How to debug when the SOC continuously Resets ?
If the SOC undergoes any reset , whether through software, hardware, the ESM, or the TIFS/DM core, then each reset status should be reflected in the RST status register. Therefore, we should first monitor the following register.
If this register shows zero and the MCU_PORz hardware output pin transitions from high to low, it indicates that the SOC has gone through a Power-On Reset (POR). For all other reset reasons, reason will be captured in the RST SRC register. Based on the reset reason, we need to investigate the source of the reset.
For example, if the device is continuously experiencing a Reset and the RST SRC register indicates that the device is going through a WarmReset due to the MAIN_WARMRESET pin. So, we should then monitor the status of the MAIN_WARMRESET pin. If this pin changes from high to low, it confirms that the SOC is resetting due to the MAIN_WARMRESET pin.

## Slide 9
RST SRC Register details