## Slide 1: Solving Machine Vision Problems with CNN’s -Case study: Steel Defect Classification
Tarkesh Pande
10/19/2021

## Slide 2: Overview
CNN’s can help solve machine vision problems in the manufacturing process on factory floor. Some Examples:
  Printed Circuit Boards Defect Detection
  Material Defects
    Classification
    Localization
    Semantic Segmentation
  Industrial Machine Tool Surface Defect Detection
Ground Truth
Test Image

## Slide 3: Steel Defect Classification
NEU Steel Defect Data Set (1800 images)
Six types of Steel Defects
  Crazing
  Rolled-in scale
  Patches
  Pitted surface
  Inclusion
  Scratches
Severstal Steel Defect Data Set (large)
  Object Detection and Semantic Segmentation
  Identify and localize the defect
Inclusion
Patches
Pitted Surface
Rolled-In Scale
Scratches
Crazing

## Slide 4: CNN Model
Design a simple CNN classifier
  (VGG style)
CNN has ~600k parameters
Six output classes
Can easily get to > 95% accuracy with a
in a few epochs with simple CNN model

## Slide 5: Evaluate on TI’s EdgeAI Cloud
https://dev.ti.com/edgeaisession

## Slide 6: Profile Custom Model
Profile both ARM and C7/MMA
Three step procedure
  Load model and Test data onto cloud
  Select tflite run-time option
  Select ARM or C7-MMA for target
Profile and run classification model
  ARM Only: 190.8ms per prediction (5 fps)
  C7/MMA: 1.09ms per prediction (914 fps)
~180x speed up when using C7/MMA over ARM only!
ARM-Only
C7/MMA

## Slide 7: Test Accuracy
Easy to test accuracy
Need to load test images to Cloud
If accuracy is not sufficient can test out
different calibration/quantization options
  Simplest option is increase bit precision to 16 bits

## Slide 8: Summary
CNN’s are very powerful functional approximators for classifying different types of defects in Machine Vision applications
Ease of use of training CNN’s followed by profiling networks on TI’s edgeAI cloud service
180x improvement in inference speed when running on TI’s deep learning accelerators compared to A72 cores!

## Slide 9: References
Huang,W.;Wei, P. A PCB Dataset for Defects Detection and Classification. arXiv 2019, arXiv:1901.08204.
https://github.com/tangsanli5201/DeepPCB
Guan, Shengqi & Lei, Ming & Lu, Hao. (2020). A Steel Surface Defect Recognition Algorithm Based on Improved Deep Learning Network Model Using Feature Visualization and Quality Evaluation. IEEE Access.
https://www.kaggle.com/c/severstal-steel-defect-detection
T Schlagenhauf, M Landwehr, J Fleischer (2021) “Industrial Machine Tool Component Surface Defect Dataset”, https://arxiv.org/abs/2103.13003