# NOV 15 release

## ISSUES

##### ISSUE 1 : TMDX654IDKEVM: 802.1Q VLAN Priority

All received frames have VLAN priority rewrited to 0.

Predefined frames for sending → send.pcap

Captured frames from IDK fail → received_fail.pcap

Captured frames success → received_success.pcap

HW:

TMDX654IDKEVM

SW:

System image from PROCESSOR-SDK-LINUX-RT-AM65X 08.00.00.02

Steps to reproduce:

1. Create SD card from SDK

2. Insert SD card and start IDK

3. Connect eth1 to different (PC) NIC

4. Start caprute on eth1 of IDK

# tcpdump -i eth1 -w received.pcap

5. Send predefined frames containing VLAN on PC ( use provided send.pcap )

e.g. # tcpreplay -i $IFNAME send.pcap

6. Stop tcpdump on IDK

# pkill tcpdump

7. Download capture from IDK (SD card) and compare sent and received frames.

Binaries for resolving the issue : icssg-prueth-fw_8_1_sdk.tar

To apply the binaries :

Uncompress the file attached and copy the binaries present in lib/firmware/ti-pruss/* to lib/firmware/ti-pruss/ folder of root partition of SD Card.

##### ISSUE 2 : First ICSSG Ethernet interface fails to rename in ~10% cases in Linux RT SDK 8.1

ICSSG Ethernet fails to rename. Log line "icssg-prueth icssg0-eth ets1 : renames from ethX" is missing and stays as ethX.

Interface rename rules :

SUBSYSTEM=="net", DEVPATH=="/devices/platform/bus@100000/bus@100000:bus@28380000/46000000.ethernet/net/*", NAME="ets0"

SUBSYSTEM=="net", ACTION=="add", KERNELS=="icssg0-eth", ATTR{phys_port_name}=="p1", NAME="ets1"

SUBSYSTEM=="net", ACTION=="add", KERNELS=="icssg0-eth", ATTR{phys_port_name}=="p2", NAME="ets1_top_unused"

SUBSYSTEM=="net", ACTION=="add", KERNELS=="icssg1-eth", ATTR{phys_port_name}=="p1", NAME="ets2"

SUBSYSTEM=="net", ACTION=="add", KERNELS=="icssg1-eth", ATTR{phys_port_name}=="p2", NAME="ets2_top_unused"

SUBSYSTEM=="net", ACTION=="add", KERNELS=="icssg2-eth", ATTR{phys_port_name}=="p1", NAME="ets3"

SUBSYSTEM=="net", ACTION=="add", KERNELS=="icssg2-eth", ATTR{phys_port_name}=="p2", NAME="ets3_top_unused"

Fail logs → ICSSG Ethernet Fail

Success logs → ICSSG Ethernet Success

Steps to reproduce:

1) Download and install SDK

2) Create SD card

3) Connect USB cable to UART

4) switch on the IDK

5) login as root

6) create /etc/udev/rules.d/70-persistent-net.rules with following content by editor you like:

SUBSYSTEM=="net", DEVPATH=="/devices/platform/bus@100000/bus@100000:bus@28380000/46000000.ethernet/net/*", NAME="ets0"

SUBSYSTEM=="net", ACTION=="add", KERNELS=="icssg0-eth", ATTR{phys_port_name}=="p1", NAME="ets1"

SUBSYSTEM=="net", ACTION=="add", KERNELS=="icssg0-eth", ATTR{phys_port_name}=="p2", NAME="ets1_top_unused"

SUBSYSTEM=="net", ACTION=="add", KERNELS=="icssg1-eth", ATTR{phys_port_name}=="p1", NAME="ets2"

SUBSYSTEM=="net", ACTION=="add", KERNELS=="icssg1-eth", ATTR{phys_port_name}=="p2", NAME="ets2_top_unused"

SUBSYSTEM=="net", ACTION=="add", KERNELS=="icssg2-eth", ATTR{phys_port_name}=="p1", NAME="ets3"

SUBSYSTEM=="net", ACTION=="add", KERNELS=="icssg2-eth", ATTR{phys_port_name}=="p2", NAME="ets3_top_unused"

7) execute "sync"

8) execute "reboot" to correctly unmount filesystem

9) switch off the IDK\

10) switch on the IDK

11) repeat 9) and 10) until you see "ets1" interface and log line "icssg-prueth icssg0-eth ets1: renamed from ethX" is missing

Patch to be applied on top of SDK : 0001-v2-drivers-net-ethernet-ti-icssg_prueth-fix-port-ren.patch

##### ISSUE 3 : Cannot get Link Settings after administrative link is down

After setting the link down, ETHTOOL returns following settings :

Settings for ethX:

Current message level: 0x00007fff (32767)

drv probe link timer ifdown ifup rx_err tx_err tl

Link detected: no

Steps to reproduce :

- Started from linux-rt SDK 8.2. Created the sd-card from compressed image in SDK.

- After booting the SD- card, if we do an `ethtool $IF` for any interface (eth0-eth6), we get the settings available for the link.

- Now, run `ifconfig $IF down`.

- Doing `ethtool $IF` for the interface which is down results in no setting being displayed

Patch to be applied on top of the SDK : tiL5.10-CON-v3-net-ti-icssg-prueth-move-phy_connect-phy_disconnect.patch

### HOW TO APPLY PATCH ?

- Go to path = <sdk-path>/board-support/linux-rt*

Command to apply patch → git am <path of patch>

ORDER of applying patches :

1. 0001-v2-drivers-net-ethernet-ti-icssg_prueth-fix-port-ren.patch

- 2. tiL5.10-CON-v3-net-ti-icssg-prueth-move-phy_connect-phy_disconnect.patch

### HOW TO BUILD ?

Go to path = <sdk-path>/board-support/linux-rt*

- Before compiling the kernel or kernel modules the SDK’s toolchain needs to be added to the PATH environment variable export PATH=<sdk path>/linux-devkit/sysroots/x86_64-arago-linux/usr/bin:$PATH

Command to clean the kernel:

- make ARCH=arm64 CROSS_COMPILE=aarch64-none-linux-gnu- distclean

- Build dconfig from kernel git repositoryti_config_fragments/defconfig_builder.sh -t ti_sdk_arm64_release export ARCH=arm64 make ti_sdk_arm64_release_defconfig

- Build Commandmake ARCH=arm64 CROSS_COMPILE=aarch64-none-linux-gnu-

Copy kernel image and device binary tree file to root partition of SD Cardcd <kernel sources dir> sudo cp arch/arm64/boot/Image /media/user/rootfs/boot sudo cp arch/arm64/boot/dts/ti/*.dtb /media/user/root/boot/

- sudo cp arch/arm64/boot/dts/ti/*.dtbo /media/user/root/boot/

- Install kernel modules on root partition of SD Cardsudo make ARCH=arm64 INSTALL_MOD_PATH=/media/user/root modules_install