## Slide 1: TI DSP
Basic Optimization
FAE Summit 2015
Ran Katzur
EP Application Team

## Slide 2: Agenda
C6000 VLIW architecture
Pipeline
Software pipeline optimization
  Estimate performances
  Using CCS to optimize code
  Software pipeline issues
Lab - Optimize FIR filter

## Slide 3: C6000 DSP Core Architecture
Memory
A0
A31
. .
.S1
.D1
.L1
.S2
.M1
.M2
.D2
.L2
B0
B31
. .
Controller/Decoder
MACs
VLIW (Very Large Instruction Word) architecture:
  Two (almost independent) sides, A and B
  8 functional units: M, L, S, D
  Up to 8 instructions sustained dispatch rate

## Slide 4: C6000 Cross-Path
A0
A1
A2
A3
A4
Register File A
. . .
B0
B1
B2
B3
B4
Register File B
. . .
A31
B31
A
.D1
.S1
.M1
.L1
B
.D1
.S1
.M1
.L1

## Slide 5: Some C6000 Family Members
TMS320C6424
TMS320C6748
TMS320C6678

## Slide 6: Partial List of .M Instructions

## Slide 7: Partial List of .D Instructions

## Slide 8: Partial List of .L Instructions

## Slide 9: Partial List of .S Instructions

## Slide 10: Agenda
C6000 VLIW architecture
Pipeline
Software pipeline optimization
  Estimate performances
  Using CCS to optimize code
  Software pipeline issues
Lab - Optimize FIR filter

## Slide 11: Non-Pipelined vs. Pipelined CPU
CPU Type
F2 D2 E2
F3 D3 E3
F1 D1 E1
Non-Pipelined
Clock Cycles
1 2 3 4 5 6 7 8 9
Pipeline full
Now look at the C66x pipeline.
Stage | Pipeline Function
F Fetch | Generate program fetch address Read opcode
D Decode | Route opcode to functional units Decode instructions
E Execute | Execute instructions
F1 D1 E1
F2 D2 E2
F3 D3 E3
Pipelined

## Slide 12: Program Fetch Phases
PW
C66x Core
PS
Memory
PG
Phase | Description
PG | Generate fetch address
PS | Send address to memory
PW | Wait for data ready
PR | Read opcode
Functional
Units
PR

## Slide 13: Pipeline Phases: Review
Single-cycle performance is not affected by adding three program fetch phases.
That is, there is still an execute every cycle.
PG PS PW PR D E
PG PS PW PR D E
PG PS PW PR D E
PG PS PW PR D E
PG PS PW PR D E
PG PS PW PR D E
Program Fetch
Execute
Decode
How about decode? Is it only one cycle?

## Slide 14: Decode Phases
Decode Phase | Description
DP | Intelligently routes instruction to functional unit (dispatch)
DC | Instruction decoded at functional unit (decode)
PW
C66x Core
PS
Memory
PR
PG
Functional
Units
DP
DC

## Slide 15: Pipeline Phases
Pipeline Full
PG PS PW PR DP DC E1
PG PS PW PR DP DC E1
PG PS PW PR DP DC E1
PG PS PW PR DP DC E1
PG PS PW PR DP DC E1
PG PS PW PR DP DC E1
PG PS PW PR DP DC E1
Program Fetch
Execute
Decode
How many cycles does it take to execute an instruction?
Notes: Should the EXECUTEs be sequential here? E1, E2. E3, etc.

## Slide 16: Instruction Delays
All C66x instructions require only one cycle to execute, but some results are delayed.
Description | Instruction Example | Delay
Single Cycle | All instructions except | 0
Integer multiplication and new floating point | MPY, FMPYSP | 1
Legacy floating point multiplication | MPYSP | 2
Load | LDW | 4
Branch | B | 5

## Slide 17: Agenda
C6000 VLIW architecture
Pipeline
Software pipeline optimization
  Estimate performances
  Using CCS to optimize code
  Software pipeline issues
Lab - Optimize FIR filter

## Slide 18: Software Pipeline Example
Void example(float *in, float*out, int N, float V)
{
sum = 1.0 ;
for (i=0; i<N; i++)
{
x = *in++ * V ;
sum = sum + x ;
*out++ = sum ;
}
}
How many cycles would it take to perform the loop five times?

## Slide 19
Implementation of the loop in the following code:
Void example(float *in, float*out, int N, float V)
{
sum = 1.0 ;
for (i=0; i<N; i++)
{
x = *in++ * V ;
sum = sum + x ;
*out++ = sum ;
}
}
Non Pipeline example
Notes: Indicate here how many cycles this code processing will require (40 cycles)

## Slide 20
Implementation of the loop in the following code:
Void example(float *in, float*out, int N, float V)
{
sum = 1.0 ;
for (i=0; i<N; i++)
{
x = *in++ * V ;
sum = sum + x ;
*out++ = sum ;
}
}
Software Pipeline example
The compiler knows all the delays and is smart enough to build the correct software pipeline

## Slide 21: Software Pipeline Support
The compiler is smart enough to schedule instructions efficiently.
Software pipeline is the major speed-up mechanism for VLIW architecture.
Software pipeline requires deterministic execution:
  Not if, branch, and call
  No interrupts
  No dependencies

## Slide 22
Implementation of the loop in the following code:
Void example(float *in, float*out, int N, float V)
{
sum = 1.0 ;
for (i=0; i<N; i++)
{
x = *in++ * V ;
sum = sum + x ;
*out++ = sum ;
}
}
Software Pipeline example Interrupt

## Slide 23
Implementation of the loop in the following code:
Void example(float *in, float*out, int N, float V)
{
sum = 1.0 ;
for (i=0; i<N; i++)
{
x = *in++ * V ;
sum = sum + x ;
*out++ = sum ;
}
}
Software Pipeline example - SPLOOP

## Slide 24: SPLOOP: Advantages & Limitations
SPLOOP Advantages:
  Enables interrupts during software pipeline
  Saves memory
  Saves power
  Implicit loop counter - saves a unit
  Nested loops are supported
  Scheduled by the compiler
SPLOOP Limitations
  Limits number of executable packets (14)
  Limits on the usage and location of some instructions (see the documentations)
  NOTE: The compiler is not always smart enough to schedule SPLOOP, especially if the minimum number of iterations is not known (to the compiler).

## Slide 25: Code Development
  Code Generation Tools can build executables from different code types:
  Generic C or C++ code
  C with intrinsic
  Linear Assembly
  Assembly (DETAI)
  Optimization is performed:
  In the front end
  Using the intrinsic
  Resource allocation and software pipeline search in optimized linear assembly
  To understand the quality of the optimization of a loop, compare the theoretical iteration interval (II: The actual number of cycles between two results of the loop) to the result of the assembler/optimizer.
  Was the software pipeline successful (if not, why)?
  Is the usage balanced between the two sides (if not, can it be improved)?
  What are the bottlenecks and how to mitigate them?
  To keep the assembly file, set the –k option

## Slide 26: Keep Generated Assembly file

## Slide 27: Build Options – Optimization and Debug

## Slide 28: -S and -MW Setting

## Slide 29: And if You Don’t Find the GUI?

## Slide 30
Implementation of the loop in the following code:
Void example(float *in, float*out, int N, float V)
{
sum = 1.0 ;
for (i=0; i<N; i++)
{
x = *in++ * V ;
sum = sum + x ;
*out++ = sum ;
}
}
Dependencies –
What if out = in + 1?
In that case the code cannot start loading the next input before the previous output is ready
Unless the compiler knows otherwise, the compiler assumes dependencies

## Slide 31: Dependencies
The compiler knows that there is no dependencies in the following cases:
  It can understand it from the code (the calling function is in the same file as the routine)
  The code use the restrict keyword
  Using compiler switch that tells the compiler that there is no overlay between vector pointers (-mt)

## Slide 32: IF and Conditional execution
  All assembly instructions are conditional instructions
  In conditional instruction the functional unit executes the instruction but the result is written to the output register ONLY if the condition is true
  The condition should be known ONLY the cycle before the result is written to the output register
  Condition execution can replace if statements as follows:
if (x < 1000.0) sum = sum + x --> [x <1000.0] sum=sum+x
  The compiler is smart enough to convert “simple” if statements into conditional execution
  The result of x < 1000.0 should known just one cycle before the last step of execution

## Slide 33
Void example(float *in, float*out, int N, float V)
{
sum = 1.0 ;
for (i=0; i<N; i++)
{
x = *in++ * V ;
sum = sum + f(x) ;
*out++ = sum ;
}
}
Function Calls
function call prevents the compiler from generating software pipeline
Inline the function removes this limitation
The compiler does not inline function (unless it is told to), it is up to the user

## Slide 34: Software Pipeline Example
void copyFunction(int *p1, int *p2, int N)
{
int i ;
for (i=0; i<N;i++)
{
*p2++ = *p1++ ;
}
return ;
}

## Slide 35: Software Pipeline Example - reminder
;*----------------------------------------------------------------------------*
;* SOFTWARE PIPELINE INFORMATION
;*
;* Loop found in file : ../utility.c
;* Loop source line : 12
;* Loop opening brace source line : 13
;* Loop closing brace source line : 15
;* Known Minimum Trip Count : 1
;* Known Max Trip Count Factor : 1
;* Loop Carried Dependency Bound(^) : 6
;* Unpartitioned Resource Bound : 1
;* Partitioned Resource Bound(*) : 2
;* Resource Partition:
;* A-side B-side
;* .L units 0 0
;* .S units 0 0
;* .D units 0 2*
;* .M units 0 0
;* .X cross paths 0 0
;* .T address paths 0 2*
;* Long read paths 0 0
;* Long write paths 0 0
;* Logical ops (.LS) 0 0 (.L or .S unit)
;* Addition ops (.LSD) 0 0 (.L or .S or .D unit)
;* Bound(.L .S .LS) 0 0
;* Bound(.L .S .D .LS .LSD) 0 1
;*
;* Searching for software pipeline schedule at ...
;* ii = 6 Schedule found with 2 iterations in parallel
;* Done
;*
;* Loop will be splooped

## Slide 36: Restrict Qualifiers
Loop iterations cannot be overlapped unless input and output are independent (do not reference the same memory locations).
Most users write their loops so that loads and stores do not overlap.
Compiler does not know this unless the compiler sees all callers or user tells compiler.
Use restrict qualifiers to notify compiler.
Restrict tells the compiler that any location addressed by the following pointer WILL NOT be accessed by any other vector.
void copyFunction(int *restrict p1, int *p2, int N)
{
int i ;
for (i=0; i<N;i++)
{
*p2++ = *p1++ ;
}
return ;
}

## Slide 37
;*----------------------------------------------------------------------------*
;* SOFTWARE PIPELINE INFORMATION
;*
;* Loop found in file : ../utility.c
;* Loop source line : 12
;* Loop opening brace source line : 13
;* Loop closing brace source line : 15
;* Known Minimum Trip Count : 1
;* Known Max Trip Count Factor : 1
;* Loop Carried Dependency Bound(^) : 0
;* Unpartitioned Resource Bound : 1
;* Partitioned Resource Bound(*) : 1
;* Resource Partition:
;* A-side B-side
;* .L units 0 0
;* .S units 0 0
;* .D units 1* 1*
;* .M units 0 0
;* .X cross paths 0 1*
;* .T address paths 1* 1*
;* Long read paths 0 0
;* Long write paths 0 0
;* Logical ops (.LS) 0 0 (.L or .S unit)
;* Addition ops (.LSD) 0 1 (.L or .S or .D unit)
;* Bound(.L .S .LS) 0 0
;* Bound(.L .S .D .LS .LSD) 1* 1*
;*
;* Searching for software pipeline schedule at ...
;* ii = 1 Schedule found with 7 iterations in parallel
;* Done
;*
;* Loop will be splooped

## Slide 38: Agenda
C6000 VLIW architecture
Pipeline
Software pipeline optimization
  Estimate performances
  Using CCS to optimize code
  Software pipeline issues
Lab - Optimize FIR filter

## Slide 39: DSP Lab Instructions