## Slide 1: AM62x – Differentiation vs AM335x
AM62x
16nmFF
64KB Shared SRAM
Power
Manager
Debug
Firewall
System
Monitor
DMA
Timers
System Services
IPC
Secure Boot
DCC ESM ECC CRC
Security Acceleration
Crypto: AES, SHA, PKA, RNG, SM2, SM3, SM4
3D Graphics Engine
Open GL3.x
Vulkan 1/x
MCU with FFI
Cortex M4F
16b DDR4/LPDDR4
w/ ECC
Display Subsystem
Up to 2K support
DPI x1; OLDI/LVDS x1
System control
& Low power
Application Cores
Arm®
Cortex A53
512KB L2$
Arm®
Cortex A53
Cortex M4F
Cortex M4F
Hardware Security Module
32K I$ / 32K D$
64K TCM
Cortex R5F
AM62x Enhancement
Arm®
Cortex A53
Arm®
Cortex A53
256KB RAM
Diagnostic toolkit: ECC, ESM, BIST, DCC, CRC
GPIO
1x I2C
2x SPI
2x CAN-FD
1x UART
PRU SS
PRU Core 0
32KB SMEM
PRU Core 1
General Connectivity & IO
Memory/Flash
GPMC
OSPI
x1
MMC/SD
x3
High-speed interfaces
2-port Gb Ethernet
w/1588 & TSN
2x USB 2.0
GPIO
SPI
x3
UART
x8
I2C
x5
CAN-FD
x1
Multimedia
McASP
x3
CSI-RX (4L)
1x
Control Peripherals
eQEP
x3
eCAP
x3
ePWM
x3
176KB
256KB
ARM Performance Enhancement:
AM335x | AM62x
1x Cortex-A8 | 1/2/4x Cortex-A53
Up to 1GHz | Up to 1.4GHz
Up to 2K DMIPS | Up to 16.8KDMIPS
DDR Enhancement:
AM335x | AM62x
DDR3/DDR3L | DDR4/LPDDR4
191MB/S | 596 MB/S
Throughput | > 3 times
GPU Enhancement:
AM335x | AM62x
SGX530 @200MHz | AXE1-16M @500MHz
1.6G FLOPS | 8G FLOPS
OpenGL ES 2.0 | OpenGL ES 3.1 Vulkan
Display Feature Enhancement:
AM335x | AM62x
Single Display | Dual Display
RGB 888 | DPI + LVDS
1080P30 | 2K (1080P60)
Secure boot
Functional safety
Peripherals Enhancement:
AM335x | AM62x
UART x 6 | UART x 9
CAN x 2 | CAN-FD x 3
I2C x 3 | I2C x 6
SPI x 2 | SPI x 5
GPMC – 100MHz | GPMC – 133MHz
New Features:
AM335x | AM62x
- | CSI-RX (4L)
- | OSPI
ETH x2 | ETH x2 (TSN)
*LMBench bw_mem 8MB/s copy Test Result
AM335x Simplification

## Slide 2: AM62x vs AM64x: Spec comparison
Feature |  | AM62x (Superset: AM6254) | AM64x (Superset: AM6442)
Processors | ARM Cores | 4x Cortex-A53 @ 1.4GHz (512KB L2 Cache) | 2x Cortex-A53 @ 1.0GHz (256KB L2 Cache)
 |  | Cortex-M4@400MHz (Functional Safety or GP processing) | 4x Cortex-R5F @ 800MHz
 |  |  | Cortex-M4@400MHz for FuSa or GP
Graphics | Display | Dual Display (24b RGB+ Open-LDI) up to 2K | Drive simple displays via SPI I/F
 | 3D GPU | Imagination AXE-1-16 3D Graphics accelerator (up to 8 GFLOPS) | No
Memory | On-chip SRAM | 64KB | 2MB
 | DDR | 16 bit DDR4/LPDDR4 w inline ECC (8/4 GB) | 16 bit DDR4/LPDDR4 w inline ECC (2GB)
Security & Safety | Safety | SIL 2 Random / SIL 3 Systematic | SIL 2 Random / SIL 3 Systematic
 | Security | Secure boot & HSM Support | Secure boot
Peripherals | PCIe Rev 2.0 | No | 1x 1L - Gen 2 (Shared PCIe/USB SerDes)
 | USB 3.0 |  | 1x USB 3.0 (Shared PCIe/USB SerDes)
 | USB 2.0 | 2x USB 2.0 | 1x USB 2.0 (Shared USB 3.1/USB2.0 port)
 | Camera I/F | 1x CSI-Rx (4-Lane) | No
 | CAN-FD | 3 | 2
 | SD/eMMC | 3 | 2
 | GPMC | 16 bit @133MHz | 16 bit @133MHz, 32 bit @ 100MHz
 | OSPI | OSPI | OSPI
 | UART | 9 | 9
 | SPI | 4 | 7
 | I2C | 6 | 6
Ethernet | Ethernet | 2x Gb Ethernet w TSN | Up to 5x Gb Ethernet w TSN
 | Industrial E-Net | Controller support only | Controller and Client support
 | PRU-SS | 2x PRU-SS | 2x PRU-ICSS-G
Motor Control | ADC | No | 1x 12 bit ADC up to 4MSPS, 8-ch
 | EPWM | 3 | 9
 | EQEP/ECAP | 3/3 | 3/3
 | FSI | No | 2TX + 6RX
Low Power Modes |  | Yes | No
Price |  | 5$ - 10$+ | 7$ - 18$
AM62x provides up to 4x A53 cores with higher frequencies, while AM64x offers multi-R5Fs to handle multiple parallel real time tasks on the Linux device.
AM62x Core Performance | AM64x Core Performance
4x A53: 16.8K DMIPS | 2x A53: 6.0K DMIPS; 4x R5F: 6.7K DMIPS
Display feature with 3D support is a key differentiation for AM62x
Thought AM64x doesn’t have on-chip display interface, but it can talk to external display modules through UART/SPI.
AM64x supports high speed interfaces, such as PCIe, USB 3.0.
Industrial Ethernet and PRU-ICSS-G support on AM64x
AM64x supports multiple industrial communication protocols w TI pre-integrated stack, EtheCAT/ProfiNET/Ethernet IP/etc, as well as encoder interfaces, such as enDAT/Biss/Tamagawa/etc. Also sigma-delta filter is supported for motor drives.
AM62x's PRU can only support serial interfaces and GPI/O for self-defined interfaces, without the industrial communication subsystem support.
Lots of motor drives application associated interfaces are also supported by AM64x well, such as ADC, PWM, FSI.
Abundant peripherals are provided by both AM62x and AM64x, check with customers’ requirement to see which part fits well.
Notes: AM64x: USB 3.0/PCIe share SerDes Lanes,
Device: SuperSpeed Gen1 (5Gbps), HS (480Mbps), FS(12Mbps)
Host: SuperSpeed Gen1 (5Gbps), HS (480Mbps), FS(12Mbps), LS (1.5 Mbps)

## Slide 3: AM62x vs AM64x: Spec comparison
Feature | Pick AM64x | Pick AM62x | Pick AM62P | Comment
Quad A53 Core @ 1.4GHz | Dual @ 1.0GHz | x | x | AM64: P2P quad A53 @ 1.4GHz device on roadmap
R5F control Loops | x | - | x | AM64: Up to 4x R5Fs @ 800MHz AM62P: 1x R5F @ 800MHz (supoprts Functional Safety or real-time control loops) Up to SIL 2 Safety Element out of Context; FFI = Freedom form Interference
M4 FFI Core @ 400MHz | x | x | - | Supports up to SIL 2 Safety Element out of Context; FFI = Freedom form Interference
ICSSG support | 2x | 1x PRU-SS | - | ICSSG provides real-time I/O support for motor control, industrial comms, buss I/F, etc.
PCIe or USB 3.0 | x | - | - | AM64: Single SERDES so it’s PCIe 2.0 or USB 3.0
2x USB 2.0 | - | x | x | AM64: Single USB 2.0 or USB 3.0 on AM64x
Industrial Comms support | Master & Slave | Master | Master | i.e. Profinet, EtherCAT, EtherNet/IP
> 2 Ethernet ports | Up to 5x | 2x | 2x | 10/100/1000 w/ TSN support
Display | - | 2x (Up to 2048 x 1080) | 3x (Up to 3840 x 1080) | AM62: Open LDI & DPI (24b RGB) video I/Fs AM62P: Open LDI, DPI (24b RGB) & DSI video I/Fs + H264/H265 video encode/decode
3D Graphics | - | Up to 8 GFLOPS | Up to 50 GFLOPS | 
Camera I/F | - | x | x | AM62: 1x CSI-Rx (4-Lane) @ 1.5Gbps-per-lane AM62P: 1x CSI-Rx (4-Lane) @ 2.5Gbps-per-lane
Memory I/F | DDR4/ LPDDR ECC (16-bit/1600MT) | DDR4/ LPDDR ECC (16-bit/1600MT) | DDR4/ LPDDR ECC (32-bit/3733MT) | 
Low Power Modes | - | x | x | 
Price | 7 to $14 | 6 to $11 | 13 to $18 | AM64x: 14 to $18 with TI provided industrial comms software stacks