## Slide 1: MSPM0G3519 Flash Bank Swap Guide
MSP HSM Apps
Sep.23, 2024

## Slide 2: Bank Swap Function Description
G3519 will include two code bank:
MCU will run in BANK0 default after POR/BOR
Bank swap function need to enable by change NONMAIN region
  Enable CSC function
  INITDONE will not auto release
Swap bank from bank0 to bank1
  Set swap bit:
  DL_SYSCTL_executeFromUpperFlashBank(); // set swap bank to bank1
  Issue INITDONE(This will trigger System Reset):
    DL_SYSCTL_issueINITDONE(); // Issue INITDOEN to trigger System Reset -> swap to bank1
Swap bank from bank1 to bank0
  Trigger BOOT Reset:
  DL_SYSCTL_resetDevice(DL_SYSCTL_RESET_BOOT); // trigger BOOT Reset -> swap to bank0

## Slide 3: Hands on
Step 1: Change NONMAIN via uniFlash

## Slide 4: Hands on
Step 2: Down app code

## Slide 5: How to Generate App Code

## Slide 6: Swap Flow
Power on
MCU Boot
Main Run in Bank0
INITDONE not release
App0 Run
Bank Swap?
Set SWAP bit
Release INITDONE
Main Run in Bank1
Bank Swap?
App1 Run
Trigger BOOT Reset
Y
N
Y
N
System Reset will be trigger, and SWAP bit will maintain
After INITDONE released, cannot change SWAP bit, and system reset will not change SWAP bit and also cannot clear INITDONE, thus have to trigger BOOT Reset to swap back to Bank0.

## Slide 7: More Resource
Secure Boot Example, will include Bank swap feature