TAS5717

PUREPATH STUDIO START UP

TAS5717 has a I2C address of 54 and needs to be changed in the user’s environment variables in the OS.  Here are the steps to make GDE talk via USB to I2C port of the TAS5717.

Go to START, My Computer, Right Click and click on Properties

On the System Properties Window, click on Advanced tab

Then click on Environment Variables button

Under User variables, if variable name PPSI2C is not there, then click New button.  If variable name PPSI2C is already there, click on PPSI2C to select it, then click Edit button.

For new variable, enter PPSI2C as variable name and 54 (for TAS5717) as variable value.

For editing, just enter 54 (for TAS5717) as variable value.

Click OK and exit out.

If you already have GDE open, close it – because it will not take effect until you close it out and reopen it.

Open GDE and go to Tools, I2C Memory Tool and select I2C tab

Read I2C subaddress 0x00 and the data should be 6C.

This verifies that you are talking to TAS5717.