## Slide 1
Order | ADD | Register | Function | Bit | R/W | Value | Note
1 | 0xC3 | HDCP_CTL | HDCP_RST | 7 | W | 1 | Resetting the HDCP registers
2 | 0xC2 | HDCP_CFG | HDCP_EESS | 6 | W | 1 | EESS mode setting
3 | 0xC7 | HDCP_ISR | IS_RXDET_INT | 6 | R | 1 | Checking the interrupt status “IS_RXDET_INT” since the interrupt is asserted. Go to next if the value is “1”.
4 | 0xC3 | HDCP_CTL | HDCP_EN | 0 | W | 1 | Authentication starts by setting “1”.
5 | 0xC7 | HDCP_ISR | IS_KSV_RDY | 3 | R | 1 | When getting the interrupt by INTB=0, check the “IS_KSV_RDY”. If it is “1”, go to #6.
6 | 0xC4 | HDCP_STS | KSV_RDY | 1 | R | 1 | If encryption key is stored, it becomes “1”. If it becomes “1”, go to next.
7 | 0x80 | RX_BKSV0 |  | 7:0 | R |  | Read the key since it is stored. Checking the read key with the HDCP content list. If it is done via HDMI, storing the encription key to HDMI_RX register. Refer to the HDMI_RX control specification for storing the registers. If it is NG, then finish authentication by authentication NG. If it is OK, go to #8.
 | 0x81 | RX_BKSV1 |  | 7:0 | R |  | 
 | 0x82 | RX_BKSV2 |  | 7:0 | R |  | 
 | 0x83 | RX_BKSV3 |  | 7:0 | R |  | 
 | 0x84 | RX_BKSV4 |  | 7:0 | R |  | 
8 | 0xC3 | HDCP_CTL | KSV_VALID | 4 | W | 1 | If it is set “1”, proceed to next process.
9 | 0xA0 | RX_BCAPS | Repeater | 6 | R | 0 | Check if there is repeater connection on deserializer side , then go to “17 after KSV_RDY=0.
10 | 0xC7 | HDCP_ISR | IS_LIST_RDY | 4 | R | 1 | If there is interrupt by INTB=0, check IS_LIST_RDY. If it is “1”, go to next.
11 | 0xC4 | HDCP_STS | KSV_LIST_RDY | 2 | R | 1 | Check if the KSV list is read.
12 | 0xA1 | RX_BSTATUS0 |  | 7:0 | R |  | Check the read value with the HDCP content list.
13 | 0xA2 | RX_BSTATUS1 |  | 7:0 | R |  | If it matches, return to #4.
14 | 0xA0 | RX_BCAPS | KSV_FIF_RDY | 5 | R |  | KSV list is ready and it shows if the checked values are calculated.
15 | 0xA3 | KSV_FIFO |  | 7:0 | R |  | Read DEVICE_CNT * 5 times.
16 | 0xC3 | HDCP_CTL | KSV_LIST_VALID | 5 | W | 1 | Write “1”.
17 | 0xC7 | HDCP_ISR | IS_AUTH_PASS | 1 | R | 1 | Check the interrupt status of “IS_AUTH_PASS”. If it is “1”, go to next.
18 | 0xC4 | HDCP_STS | AUTHED | 0 | R | 1 | After detecting INTB=0, go to next if this is “1”.
19 | 0xC3 | HDCP_CTL | HDCP_ENC_EN | 2 | W | 1 | The protected contents can be sent by writing “1”.
20 |  |  |  |  |  |  | Check the INTB to confirm if the authentication is lost. Check the interrupt status of “IS_AUTH_FAIL”. If it becomes “L”, return to #4.