## Slide 1: GC1115 Crest Factor Reduction Processor A Texas Instruments Digital Signal Processing Solution
Wireless Infrastructure Business Unit May 2005

## Slide 2: GC1115 Crest Factor Reduction Processor
Systems Overview
GC1115 Block Diagram
Peak Detection & Cancellation Pulse Generation
GC1115 Architecture
Single-carrier 3GPP Test Model Results
Power Amp Measurements: Output Power Improvement
Multi-carrier 3GPP Test Model Results
Varying Carrier Power Results
Summary

## Slide 3: GC1115 Crest Factor Reduction Processor
20 MHz CFR processor for  4 UMTS or  15 cdma2000 carriers
Flexible input and output modes (parallel/muxed; 2’s comp/unsigned)
Supports one or two channels (Tx diversity); real or complex cancellation coefficients
User-specified output peak-to-average (PAR) levels and cancellation pulse coefficients
D/A
PA
GC5016
GC5316
DUC
Micro-cntrl
or
TI DSP
GC1115
RF
Upconverter

## Slide 4: Crest Factor Reduction Increases Efficiency
Vin
Vout
13 dB input PAR
1 dB compression point
(maximum output)
Input signal
average power
(0 dB point)
7 dB
output PAR
GC1115 provides
6 dB peak
reduction
Avg PA output (10 W)
AC wall power (125 W)
= 8%
Efficiency Before GC1115

## Slide 5: Crest Factor Reduction Increases Efficiency
Efficiency After GC1115
Vin
Vout
13 dB input PAR
1 dB compression point
(maximum output)
Input signal
average power
Apply 6 dB gain
to GC1115 output
Avg PA power (20 W)
AC wall power (125 W)
= 16%
7 dB
output PAR
Output signal
average power

## Slide 6: GC1115 Block Diagram

## Slide 7: GC1115 Crest Factor Reduction Processor
“Smart” peak detection and cancellation minimizes the distortion introduced through CFR.
Real or complex cancellation modes can be used accommodating asymmetric waveforms.
Time domain
Frequency domain
Four 5 MHz carriers active; centered at –7.5, -2.5, +2.5, +7.5 MHz
Two of four 5 MHz carriers active; centered at –2.5 MHz, +7.5 MHz

## Slide 8: GC1115 Crest Factor Reduction Processor
The following figure illustrates a simplified version of peak detection and cancellation
+
-
Input Signal
Cancellation Signal
Output Signal

## Slide 9: GC1115 Crest Factor Reduction Processor
Detection threshold
Gain threshold
Typical time analysis of interpolated peak detection and reduction:

## Slide 10: GC1115 Crest Factor Reduction Processor
Output PAR @ 10-4: 8.0 dB
Input PAR @ 10-4: 10.7 dB
Peak reduction: 2.7 dB
CFR performance is measured using a complementary cumulative distribution function (CCDF), the result is quantified as the PAR of the signal.

## Slide 11: GC1115 Crest Factor Reduction Processor
Software, EVM platform, and Test &Measurement hardware or software can be used for design and optimization.
FSU
Agilent ADS/SS SW
TI EVM Platform GC101 Board, GC1115 Plugin; and GC Studio SW
GC1115 and signal performance are measured in software using Agilent ADS/VSA and/or hardware using a spectrum analyzer.
Performance is quantified for target PAR levels versus composite error vector magnitude (cEVM) and peak-code domain error (PCDE).
Agilent ADS/VSA
TI EVM HW:
DAC or DAC/RF; DAC5687,TSW3000

## Slide 12: GC1115 Crest Factor Reduction Processor
Output average power is lower than input average power due to GC1115 peak reduction.
Vin
Vout
5dB
5.7dB
0.7dB
Average power
of output signal
Average power
of input signal
Peak power
of output signal
Target PAR | Output PAR | Relative Output Average Power
5dB | 5.7dB | -0.7dB
6dB | 6.4dB | -0.4dB
7dB | 7.02dB | -.02dB

## Slide 13: GC1115 Crest Factor Reduction Processor
-Test Model 1_64 (ACLR[with spectrum analyzer], CEVM)
Test Model 3_32 (PCDE)
Test Model 5 (HSDPA-CEVM)
CFR Measurements for WCDMA, UMTS
Example configurations are provided with GC Studio software, built from the ADS 3GPP test sources or from a Digital Up Converter, GC5016, GC5316
The following test models were used:

## Slide 14: GC1115 Crest Factor Reduction Processor
TM1_64 Single Carrier-All Digital Measurements
- | Input | 8 dB | 7 dB | 6 dB | 5db
PCDE | -66 | -50.2 | -44.9 | -41.3 | NM
cEVM | .5% | 2.4% | 4.8% | 7.2% | NM

## Slide 15: GC1115 Crest Factor Reduction Processor
TM1_64 Multicarrier - All Digital Measurements
- | Input | 8 dB | 7 dB | 6 dB | 5db
PCDE | -65 | -48.9 | -43.3 | -38.7 | NM
cEVM | .5% | 3.2% | 6.3% | 10.3% | NM
The worst carrier of the multicarrier is reported in the table.
The coefficient design, input and output modes, and symmetric
or assymmetric affect the performance.
2 carrier Non symmetric around 0IF
- | Input | 8 dB | 7 dB | 6 dB | 5db
PCDE | -65.2 | -47.6 | -43.2 | -39.6 | NM
cEVM | .5% | 3.9% | 6.3% | 9.4% | NM
3 carrier Non symmetric around 0IF
- | Input | 8 dB | 7 dB | 6 dB | 5.7db
PCDE | -65.3 | -51.6 | -46.7 | -42.9 | -41.4
cEVM | .5% | 2.4% | 4.1% | 6.6% | 7.6%
4 carrier symmetric around 0IF

## Slide 16: GC1115 Crest Factor Reduction Processor
TM1_64 CFR 6db Measured Output VSA

## Slide 17: GC1115 Crest Factor Reduction Processor
TM3_32 Single Carrier-All Digital Measurements
- | Input | 8 dB | 7 dB | 6 dB | 5 dB
PCDE | -69.4 | -48.7 | -43.2 | -39.8 | NM
cEVM | .5% | 3.3% | 5.7% | 8.7% | NM

## Slide 18: GC1115 Crest Factor Reduction Processor
TM3_32 Multicarrier - All Digital Measurements
- | Input | 8 dB | 7 dB | 6 dB | 5db
PCDE | -69 | -41.6 | -37.6 | -34.3 | NM
cEVM | .5% | 7.6% | 11.5% | 16.3% | NM
The worst carrier of the multicarrier is reported in the table.
The coefficient design, input and output modes, and symmetric
or assymmetric affect the performance.
2 carrier Non symmetric around 0IF
- | Input | 8 dB | 7 dB | 6 dB | 5db
PCDE | -68.7 | -45.3 | -40.6 | -37.8 | NM
cEVM | .5% | 4.6% | 7.9% | 11.5% | NM
3 carrier Non symmetric around 0IF
- | Input | 8 dB | 7 dB | 6 dB | 5.7db
PCDE | -68.7 | -49.3 | -44.6 | -41.5 | -40.6
cEVM | .5% | 3.5% | 5.7% | 8.5% | 9.5%
4 carrier symmetric around 0IF

## Slide 19: GC1115 Crest Factor Reduction Processor
TM3_32 CFR 7db Measured Output VSA

## Slide 20: GC1115 Crest Factor Reduction Processor
TM5_30 2 Carrier GC Studio SW Display

## Slide 21: GC1115 Crest Factor Reduction Processor
TM5_30 Multicarrier - All Digital Measurements
- | Input | 8 dB | 7 dB | 6 dB | 5db
PCDE | -57.7 | -38.4 | -34.6 | -31.6 | NM
cEVM | .5% | 4.7% | 7% | 9.7% | NM
The worst carrier of the multicarrier is reported in the table.
The coefficient design, input and output modes, and symmetric
or assymmetric affect the performance.
2 carrier symmetric around 0IF

## Slide 22: GC1115 Crest Factor Reduction Processor
TM5_30 CFR 6db Measured Output VSA

## Slide 23: GC1115 Crest Factor Reduction Processor
Items to Consider in Design Stage
1 or 2 channels are supported
Input Mode – Parallel IQ, Interleaved IQ, input rate < 130Msps
Input Decimation – Decimation of 2, if Complex Rate > 80Msps
Power Meter – can sample input, CFR stage, or output
Canceller Coefficients – support for symmetric carrier, and assymetric carrier configuration; symmetric from 31-509 coefficients, asymmetric from 31 to 255 coefficients
Interpolation / Output Mode – The output can be complex or real. The real output can be full or double rate. The complex output can be parallel IQ or interleaved IQ. Interpolation options are complex 2, complex 4, complex to real, output rate < 130Msps
Input External Sync is required, special sync for interleaved IQ input mode also
Interface of Interleaved IQ input requires special synchronization
Current Silicon requires 2 wire control port interface mode
critical output timing needs to be calculated for Tsu and Thi of receiving device

## Slide 24: GC1115 Crest Factor Reduction Processor
Summary of Features
GC1115 is a novel one-channel or two-channel CFR solution
GC1115 exceeds all 3GPP requirements (PCDE, EVM, ACLR) for PAR settings down to 6 dB
Performance meaured single-carrier UMTS, and multi-carrier UMTS, with both fixed and varying carrier power
User specifies output PAR and cancellation pulse coefs
Optional complex-to-real output, including two fs/4 options
256-pin BGA package (17 x 17 mm)
Hardware and software available for evaluation and optimization
~2 W max power consumption

## Slide 25: Conclusion Questions and Comments?